xCAT 2 How to Install Additional Software
01/07/10, 11:01:05 AM

# Introduction
xCAT 2 Cookbook illustrates how you can install the operating systems on the nodes. There are times you want to install addition software. This document explains how you can add additional software into the cluster for both stateful and stateless cases. It will also introduce a new command called 'updatenode' to allow you to configure or reconfigure the nodes. Please note all the discussion below except chapter 5 is for Linux only. There are a lot of differences in AIX. Please refer to “xCAT2 AIX Cookbook” for related topics in AIX.

# Install Additional Software for Stateless Nodes
1. copy the extra rpms you are going to add on to
 /install/post/otherpkgs/<os>/<arch>/* directory or its subdirectories where <os> and <arch> are defined in the nodetype table.
Use the following command to find out <os> and <arch> for a node.
  nodels node1 nodetype.os nodetype.arch

2. add rpm names (without version number) with their subdirectories into
 /install/custom/netboot/<ostype>/profile.otherpkgs.pkglist where
<profile> is defined in the nodetype table. <ostype> is the operating system name without the version number. The following os types are recognized by xCAT.
centos
fedora
rh
sles
windows

 Note: The default package lists are usually stored under
 /opt/xcat/share/xcat/netboot/<ostype>/ directory.

For example, file /install/custom/netboot/sles/compute.otherpkgs.pkglist will look like this if you want to add RSCT packages (src, rsct.core and rsct.core.utils):
  src
  rsct.core
  rsct.core.utils
If you have copied the rpms into a subdirectory, say rsct, then the file should be look like this:
  rsct/src
  rsct/rsct.core
  rsct/rsct.core.utils
Please see Appendix for the format of a otherpkgs.pkglist file.

3.run /opt/xcat/share/xcat/netboot/<ostype>/genimage, the extra rpms are automatically installed into the image. Then run packimage.

4.if you have additional configuration scripts for the software that would like to run after the node is boot up, copy the script to /install/postscripts directory and add the confirmation script to the postscripts table.
    cp myconfigsctipt /install/postscripts/
  chtab node=compute postscripts.postscripts=myconfigsctipt

After setting up, deploy the node as usual. The addition software will be installed and configured during the node deployment.

# Install Additional Software for Stateful Nodes

1. Copy the extra rpms you are going to add on to
 /install/post/otherpkgs/<os>/<arch>/* directory or its subdirectories where <os> and <arch> are defined in the nodetype table.
Use the following command to find out <os> and <arch> for a node.
  nodels node1 nodetype.os nodetype.arch

2. [only for Linux]
You should create repodata for the /install/post/otherpkgs/<os>/<arch>/ directory. The repodata is necessary for “yum” and “zypper” to know about the repository.

The command “createrepo” is used to create repodata, before executing the command, please make sure the “createrepo” rpm package is installed. Remember that on SLES11, the “createrepo” rpm package is in the SLE-11-SDK-DVD Media 1 ISO, not in the install ISO.

After “createrepo” is installed, run the following command to create repodata for the directory /install/post/otherpkgs/<os>/<arch>/.
 createrepo /install/post/otherpkgs/<os>/<arch>/

3. Add rpm names (without version number) with their subdirectories into
 /install/custom/install/<ostype>/profile.otherpkgs.pkglist where
<profile> is defined in the nodetype table. <ostype> is the operating system name without the version number. The following os types are recognized by xCAT.
centos
fedora
rh
sles
windows

 Note: The default package lists are usually stored under
 /opt/xcat/share/xcat/install/<ostype>/ directory.

For example, file /install/custom/install/sles/compute.otherpkgs.pkglist will look like this if you want to add RSCT packages (src, rsct.core and rsct.core.utils):
  src
  rsct.core
  rsct.core.utils
If you have copied the rpms into a subdirectory, say rsct, then the file should be look like this:
  rsct/src
  rsct/rsct.core
  rsct/rsct.core.utils
Please see the Appendix for the format of an otherpkgs.pkglist file.

4. If 'otherpkgs' is not already in the postscripts table, add it to either the xcatdefaults row or a row specifically for your node or nodegroup. The otherpkgs script name should be added to the postbootscripts attribute (for newer xcat releases) or the postscripts attribute (for older xcat releases). For example:
chtab node=compute postscripts.postbootscripts+=otherpkgs

5. If you have additional configuration scripts for the software that would like to run after the node is booted up, copy the script to /install/postscripts directory and add the configuration script to the postscripts table. For example:
    cp myconfigsctipt /install/postscripts/
  chtab node=compute postscripts.postbootscripts+=myconfigsctipt

After setting this up, deploy the node as usual. The addition software will be installed and configured during the node deployment.

# Install Additional Software for Stateless Nodes after the Nodes are Up and Running

1. follow step 1-4 in chapter 3.

2. run updatenode command
  updatenode <noderange> otherpkgs

If you have a configuration script (as mentioned in step 5 of the previous chapter), run
  updatenode <noderange> otherpkgs,myconfigscript

# Rerun Postscripts or Run Additional Scripts with the updatenode Command

You can use updatenode command to perform the following functions after the nodes are up and running:
- install additional software for stateful nodes (described in chapter 4)
- run postscripts defined in the postscripts table for both stateful and stateless nodes.
- run any script for both stateful and stateless nodes.
  The later 2 functions works on AIX as well.
  The following are some examples of how to use it:
  To re-run all the postscripts for the nodes:
  updatenode <noderange>
  To re-run the syslog postscripts for the nodes:
  updatenode <noderange> syslog
  To run a list of scripts, make sure the scripts are copied to /install/postscripts directory, then
  updatenode <noderange> script1,script2
  Note: script1,script2 may or may not be defined in the postscripts table. However if you want script1 and script2 get invoked next time the nodes are deployed, add them into the postscripts table.

# Appendix: File Format for otherpkgs.pkglist File

The otherpkgs.pklist file can contain the following types of entries:
- rpm name without version numbers
- otherpkgs subdirectory plus rpm name
- blank lines
- comment lines starting with “#”
- #INCLUDE: <full file path># to include other pkglist files
- #NEW_INSTALL_LIST# to signify that the following rpms will be installed with a new rpm install command (zypper, yum, or rpm as determined by the function using this file)
- rpms to remove before installing marked with a “-”
- rpms to remove after installing marked with a “--”
These are described in more detail in the following sections.

  1. RPM Names
A simple otherpkgs.pkglist file just contains the the name of the rpm file without the version numbers.
For example, if you put the following three rpms under /install/post/otherpkgs/<os>/<arch>/ directory,
    rsct.core-2.5.3.1-09120.ppc.rpm
    rsct.core.utils-2.5.3.1-09118.ppc.rpm
    src-1.3.0.4-09118.ppc.rpm
The otherpkgs.pkglist file will be like this:
   src
   rsct.core
   rsct.core.utils

  1. RPM Names with otherpkgs Subdirectories

If you create a subdirectory under /install/post/otherpkgs/<os>/<arch>/, say rsct, the otherpkgs.pkglist file will be like this:
  rsct/src
  rsct/rsct.core
  rsct/rsct.core.utils

  1. Include Other pkglist Files

The #INCLUDE statement is supported in xCAT 2.3 and later.

You can group some rpms in a file and include that file in the otherpkgs.pkglist file using #INCLUDE:<file># format.
  rsct/src
  rsct/rsct.core
  rsct/rsct.core.utils
  #INCLUDE:/install/post/otherpkgs/myotherlist#
where /install/post/otherpkgs/myotherlist is another package list file that follows the same format.

Note the trailing “#” character at the end of the line. It is important to specify this character for correct pkglist parsing.

  1. Multiple Install Lists

The #NEW_INSTALL_LIST# statement is supported in xCAT 2.4 and later.

You can specify that separate calls should be made to the rpm install program (zypper, yum, rpm) for groups of rpms by specifying the entry “#NEW_INSTALL_LIST# on a line by itself as a separator in your pkglist file. All rpms listed up to this separator will be installed together. You can have as many separators as you wish in your pkglist file, and each sublist will be installed separately in the order they appear in the file.

For example:
compilers/vacpp.rte
compilers/vac.lib
compilers/vacpp.lib
compilers/vacpp.rte.lnk
#NEW_INSTALL_LIST#
pe/IBM_pe_license

  1. Remove RPMs Before Installing

The “-” syntax is supported in xCAT 2.3 and later.

You can also specify in this file that certain rpms to be removed before installing the new software. This is done by adding '-' before the rpm names you want to remove. For example:
  rsct/src
  rsct/rsct.core
  rsct/rsct.core.utils
  #INCLUDE:/install/post/otherpkgs/myotherlist#
    -perl-doc

If you have #NEW_INSTALL_LIST# separators in your pkglist file, the rpms will be removed before the install of the sublist that the “-<rpmname>” appears in.

  1. Remove RPMs After Installing

The “--” syntax is supported in xCAT 2.3 and later.

You can also specify in this file that certain rpms to be removed after installing the new software. This is done by adding '--' before the rpm names you want to remove. For example:
pe/IBM_pe_license
--ibm-java2-ppc64-jre

If you have #NEW_INSTALL_LIST# separators in your pkglist file, the rpms will be removed after the install of the sublist that the “--<rpmname>” appears in.