xCAT 2 Cookbook for Linux on IBM System P

Date: 04/16/2009

Contents

# Introduction
This cookbook introduces how to use the xCAT2 to install Linux on the IBM power series machines.
The power series machines have the following characteristics:
1. May have multiple LPARs (an LPAR will be the target machine to install an operating system image on, i.e. the LPAR will be the compute node);
2. The Ethernet card and SCSI partition can be virtual devices;
3. An HMC or IVM is used for the HCP (hardware control point)

xCAT supports two types of installations for compute nodes: Diskfull installation (Statefull) and Diskless (Stateless). xCAT also supports hierarchical management clusters where one or more service nodes are used to handle the installation and management of compute node. Please refer to xCAT2advanced.pdf for hierarchical usage.
Based on the two types of installation, the following installation scenarios will be described in this document:
1. Install a stateful compute node
2. Install a stateless compute node

To provide the easier understanding of the installation steps, this cookbook provides an example to introduce the xCAT management operations:

The management node:
Arch: an LPAR on a p5/p6 machine
OS: Red Hat 5.2
Hostname: pmanagenode
IP: 192.168.0.1
HCP: HMC

The management Network:
Net: 192.168.0.0
NetMask: 255.255.255.0
Gateway: 192.168.0.1
Cluster-face-IF: eth1
dhcpserver: 192.168.0.1
tftpserver: 192.168.0.1
nameservers: 192.168.0.1

The compute nodes:
Arch: an LPAR on a p5/p6 machine
OS: Red Hat 5.2
HCP: HMC

Hostname: pnode1 – this node will be installed in stateful
IP: 192.168.0.10
Cluster-face-IF: eth0

Hostname: pnode2 – this node will be installed in stateless
IP: 192.168.0.20
Cluster-face-IF: eth0

The Hardware Control Point:
Name: hmc1
IP: 192.168.0.100

xCAT version:
xCAT-2.1+

# Install xCAT 2 on the Management node
Before preceding to setup your pLlinux Cluster, you should first read xCATtop for information on downloading and installing xCAT on your Management Node.
# Setup the management node
## [Power 5] Workaround the atftpd issue
The tftp client in the open firmware of p5 is only compatible with tftp-server instead of atftpd which is required by xCAT2. So we have to remove the atftpd first and then install the tftp-server. This is not required for p6 or later.
### Remove atftp
service tftpd stop
rpm --nodeps -e atftp
### Install the tftp server needed by xCAT, and restart it
[RH]:
yum install tftp-server.ppc

[SLES]:
zypper install tftp-server.ppc
### Restart the tftp server
Notes: make sure the entry "disable=no" in the /etc/xinetd.d/tftp.
service xinetd restart
## Setup common attributes for xCAT in the database
### Add the default account for system
chtab key=system passwd.username=root passwd.password=cluster
### Add the default account for hmc
chtab key=hmc passwd.username=hscroot passwd.password=abc123
## Define the compute nodes
The definition of a node is stored in several tables of the xCAT database.
You can use rscan command to discover the HCP to get the nodes that managed by this HCP. The discovered nodes can be stored into a stanza file. Then edit the stanza file to keep the nodes which you want to create and use the mkdef command to create the nodes definition.
### Gather Node information using the rscan command
#### Define HMC as an xCAT node
First, define the hardware control point as a node object.
The following command will create an xCAT node definition for an HMC with a host name of “hmc1”. The groups, nodetype, mgt, username, and password attributes will be set.
mkdef –t node –o hmc1 groups=hmc,all nodetype=hmc mgt=hmc	username=hscroot password=abc123
#### Discover the LPARs managed by HMC
Run the rscan command to gather the LPAR information. This command can be used to display the LPAR information in several formats and can also write the LPAR information directly to the xCAT database. In this example we will use the “-z” option to create a stanza file that contains the information gathered by rscan as well as some default values that could be used for the node definitions.
To write the stanza format output of rscan to a file called “node.stanza” run the following command.
rscan –z hmc01 > node.stanza

This file can then be checked and modified as needed. For example you may need to add a different name for the node definition or add additional attributes and values.
Note: The stanza file will contain stanzas for things other than the LPARs. This information must also be defined in the xCAT database. It is not necessary to modify the non-LPAR stanzas in any way.
The stanza file will look something like the following.
Server-9117-MMA-SN10F6F3D:
        objtype=node
        nodetype=fsp
        id=5
        model=9118-575
        serial=02013EB
        hcp=hmc01
        pprofile=
        parent=Server-9458-10099201WM_A
        groups=fsp,all
        mgt=hmc

pnode1:
        objtype=node
        nodetype=lpar,osi
        id=9
        hcp=hmc1
        pprofile=lpar9
        parent=Server-9117-MMA-SN10F6F3D
        groups=all
        mgt=hmc
        cons=hmc

pnode2:
        objtype=node
        nodetype=lpar,osi
        id=7
        hcp=hmc1
        pprofile=lpar6
        parent=Server-9117-MMA-SN10F6F3D
        groups=all
        mgt=hmc
        cons=hmc

Note: The rscan command supports an option to automatically create node definitions in the xCAT database. To do this the LPAR name gathered by rscan is used as the node name and the command sets several default values. If you use the “-w” option make sure the LPAR name you defined will be the name you want used as your node name.
For a node which was defined correctly before, you can use the “lsdef –z [nodename]> node.stanza” command to export the definition into the node.stanza, and use command “cat node.stanza | chdef -z” to update the node.stanza according to your need.
#### Define xCAT node using the stanza file
The information gathered by the rscan command can be used to create xCAT node definitions.

cat node.stanza | mkdef –z
### Update the attributes of the node
#### Set the resource attributes of the node
chdef -t node -o pnode1 netboot=yaboot tftpserver=192.168.0.1 nfsserver=192.168.0.1 monserver=192.168.0.1 xcatmaster=192.168.0.1 installnic="eth0" primarynic="eth0"

Note: Please make sure the attributes "installnic" and "primarynic" are set up by the correct Ethernet Interface of compute node. Otherwise the compute node installation may hang requesting information from an incorrect interface.
#### Set the type attributes of the node
[RH]
chdef -t node -o pnode1 os=<os> arch=ppc64 profile=compute.ppc64
[SLSE]
chdef -t node -o pnode1 os=<os> arch=ppc64 profile=compute

Note: The <os> can be rh*, centos*, fedora*, sles*. (where * is the version #) For example, the <os> can be rhels5.2 or sles11.

#### Modify the table postscripts
This only needs to be done when you want to run the my_script after installing the compute node.
chdef -t node -o pnode1 postscripts=my_scrip

## Setup the Services and Definition
The part should be experienced, when there are compute nodes, hmcs, networks defined/deleted.
### Create the xCAT network object
Create the networks that used for cluster management:
mkdef -t network -o net1 net=192.168.0.0 mask=255.255.255.0 gateway=192.168.0.1 mgtifname=eth1 dhcpserver=192.168.0.1 tftpserver=192.168.0.1 nameservers=192.168.0.1

### Setup the DNS
#### Setup /etc/hosts with entries for all you nodes, hmcs, fsps
127.0.0.1	localhost
192.168.0.1	pmanagenode
192.168.0.10	pnode1
192.168.0.20	pnode2
192.168.0.100	hmc1
#### Setup the nameserver
Add following lines into /etc/resolv.conf
search cluster.net
nameserver 192.168.0.1
#### Setup the DNS attributes in the Site table
Setup local machine as nameserver:
chdef -t site nameservers=192.168.0.1

Setup the external nameserver:
chdef -t site forwarders=9.114.1.1

Setup the local domain name:
chdef -t site domain=cluster.net

#### Setup DNS configuration
makedns
service named start
chkconfig --level 345 named on
### Configure conserver
makeconservercf
#### Set conserver attributes for the nodes
If the cons attribute for the nodes is not set by rscan, then do the following:

chdef -t node -o pnode1 cons=hmc conserver=<management node>

Note: conserver=<management node> is the default, so it is optional to set.
### Check rcons(3.4.3 and 3.4.4 are MUST to do, rnetboot and getmacs depend on it)
rcons pnode1
If it works ok, you will get into the console interface of the pnode1.

Please run this command to monitor the installation before getmacs/rnetboot, otherwise, rcons will interrupt getmacs/rnetboot procedure.

### Update the mac table with the address of the node(s)
If there's only one Ethernet adapter on the node or you have specified the installnic or primarynic attribute of the node, using following command can get the correct mac address.
getmacs pnode1

But, if there're more than one Ethernet adapters on the node, and you don't know which one has been configured for the installation process, you have to specify more parameters like this for Lpar to try to figure out an available interface by ping operation:
getmacs pnode1 -S 192.168.0.1 -G 192.168.0.1 -C 192.168.0.10

The output looks like following:
pnode1:
 Type Location Code MAC Address Full Path Name Ping Result Device Type

ent U9133.55A.10E093F-V4-C5-T1 f2:60:f0:00:40:05 /vdevice/l-lan@30000005 virtual

And the Mac address will be written into the xCAT mac table.

Warning: Before run getmacs, make sure the node is off. If not, please force the lpar shutdown with “rpower pnode1 off” command. The reason is that HMC has one issue that cannot shutdown linux nodes which is in running state.

### Check rpower is working on the node
rpower pnode1 stat
### Setup dhcp service
#### Setup the dhcp listen interfaces in site table
chdef -t site dhcpinterfaces='pmanagenode|eth1'

#### [SLES] Check the installation of dhcp-server
On the SLES management node, the dhcp-server rpm may not have been automatically installed. Use following command to check whether it has been installed:
rpm -qa | grep -E "^dhcp-server"

If it is not installed, installed it manually:
zypper install dhcp-server

#### Configure the DHCP
Add the relevant networks into the DHCP configuration:
makedhcp -n

Add the defined node into the DHCP configuration:
makedhcp -a

Restart he dhcp service:
service dhcpd restart

Note: Please make sure there is only one dhcpd server can server these compute nodes.

# Install a Compute Node
## Prepare the installation source
You can use the iso file of the installed OS to extract the installation files. For example, you have a iso file /iso/RHEL5.2-Server-20080430.0-ppc-DVD.iso
copycds /iso/RHEL5.2-Server-20080430.0-ppc-DVD.iso

Note: If you encounter the issue that the iso cannot be mounted by the copycds command. Make sure the SElinux is disabled.
## Statefull Node installation
### Customize the installation profile
xCAT uses KickStart or AutoYaST installation profile and related installation scripts to complete the installation and configuration of the compute node.
You can find the template and sample profiles in following directories:
/opt/xcat/share/xcat/install/<os>/

Commonly for installing the ppc64 compute node, you can use the compute profile.

If you want to customize the profile for compute node like <profile>.myprofile, you can copy the compute to the following directory, and make your modification base on it.
/install/custom/install/<arch>/

Note: The profile name in the <profile> can be set to certain compute node by following command:
chdef -t node -o pnode1 profile=<profile>
#### Install the specific packages
If you want to install the specific package like specific.rpm onto the compute node, copy the specific.rpm into the following directory:
/install/post/otherpkgs/<os>/<arch>
### Set the node status to ready for installation
nodeset pnode1 install
### Use network boot to start the installation
rnetboot pnode1
### Check the installation results
1. Check that ssh service on the node is working and you can login without password
2. If ssh is working but cannot login without password, force exchange the ssh key to the compute node using xdsh:
xdsh pnode1 -K

After exchanging ssh key, following command should work.
xdsh pnode1 date
## Stateless node installation
### Generate the stateless image for compute node
Typically, you can build your stateless compute node image on the Management Node if it will have the same OS and architecture with the node. If you need another OS image or architecture than the OS installed on the Management Node, you will need a machine that meets the OS and architecture you want for the image and create the image on that node.
#### Make the compute node packaging list
If you want to exclude certain package, add it into the following exlist file:
/install/custom/netboot/<os>/<profile>.exlist

Add the packages name that need to be installed on the stateless node into the pkglist file
/install/custom/netboot/<os>/<profile>.pkglist

Note: you can use the sample here: /opt/xcat/share/xcat/netboot/<os>/
[RH]:
Add following packages name into the <profile>.pkglist
    bash
    nfs-utils
    stunnel
    dhclient
    kernel
    openssh-server
    openssh-clients
    busybox-anaconda
    wget
    vim-minimal
    ntp

You can add any other packages that you want to install on your compute node. For example, if you want to have userids with passwords you should add the following:
    cracklib
    libuser
    passwd

[SLES11]:
Add following packages name into the <profile>.pkglist
    aaa_base
    bash
    nfs-utils
    dhcpcd
    kernel
    openssh
    psmisc
    wget
    sysconfig
    syslog-ng
    klogd
    vim

#### Run image generation
[RHEL]:
cd /opt/xcat/share/xcat/netboot/rh
./genimage -i eth0 -n ibmveth -o rhels5.2 -p compute

[SLES11]:
cd /opt/xcat/share/xcat/netboot/sles
./genimage -i eth0 -n ibmveth -o sles11 -p compute

#### Pack the image
[RHEL]:
packimage -o rhels5.2 -p compute -a ppc64
[SLES]:
packimage -o sles11 -p compute -a ppc64
### Set the node status ready for network boot
nodeset pnode2 netboot
### Use network boot to start the installation
rnetboot pnode2
### Check the installation result
1. Check that ssh service on the node is working and you can login without password
2. If ssh is working but cannot login without password, force exchange the ssh key to the compute node using xdsh:
xdsh pnode1 -K

After exchanging ssh key, following command should work.
xdsh pnode1 date

# Firmware upgrade
## Requirements
POWER5 and POWER6 Licensed Internal Code updates must meet the following prerequisites:
### Enable the HMC to allow remote ssh connections.
[AIX]
Ensure that ssh is installed on the AIX xCAT management node. If you are using an AIX management node, make sure the value of "useSSHonAIX" is “yes” in the site table.
chtab key="useSSHonAIX" site.value=yes
### Define the necessary attributes
The Lpar , CEC, or BPA has been defined in the nodelist, nodehm, nodetype, vpd, ppc tables.
### Define the HMC as a node
Define the HMC as a node on the management node. For example,
nodeadd hmc01.clusters.com groups=hmc
### Setup SSH connection to HMC
Run the rspconfig command to set up and generate the ssh keys on the xCAT management node and transfer the public key to the HMC. You must also manually configure the HMC to allow remote ssh connections. For example:
rspconfig hmc01.clusters.com sshcfg=enable
### Get the Microcode update package and associated XML file
Download the Microcode update package and associated XML file from the IBM Web site: http://www14.software.ibm.com/webapp/set2/firmware/gjsn.

## Perform Firmware upgrade for CEC on P5/P6
### Define the CEC as a node on the management node

Update the xCAT required xCAT tables:

Modify the nodelist table
nodeadd Server-m_tmp-SNs_tmp groups=hmc,all

Modify the table nodehm
chtab node="Server-m_tmp-SNs_tmp" nodehm.mgt="hmc"

Modify the table nodetype:
chtab node="Server-m_tmp-SNs_tmp" nodetype.nodetype="fsp"

Modify the table ppc:
chtab node="Server-m_tmp-SNs_tmp" ppc.hcp= hmc01.clusters.com

Modify the tab vpd:
chtab node=Server-m_tmp-SNs_tmp vpd.serial=s_tmp vpd.mtm=m_tmp

Set the account of the HMC(Modify the ppchcp):
chtab hcp=hmc01.clusters.com ppchcp.username=hscroot ppchcp.password=abc123

### Setup SSH connection to HMC
Generate the ssh keys on the xCAT management node and transfer the public key to the HMC to configure the HMC to allow remote ssh connections.
rspconfig hmc01.clusters.com sshcfg=enable

### Check firmware level
rinv Server-m_tmp-SNs_tmp firm

### Update the firmware

Download the Microcode update package and associated XML file from the IBM Web site: http://www14.software.ibm.com/webapp/set2/firmware/gjsn. Create the /tmp/fw directory, if necessary, and copy the downloaded files to the /tmp/fw directory.

Run the rflash command with the --activate flag to specify the update mode to perform the updates.（Please see the “rflash” manpage for more information）
rflash Server-m_tmp-SNs_tmp -p /tmp/fw --activate disruptive

NOTE:You Need check your update is concurrent or disruptive here!! other commands sample:
rflash Server-m_tmp-SNs_tmp -p /tmp/fw --activate concurrent

Notes:
1)If the noderange is the group lpar, the upgrade steps are the same as the CEC's.
2)System p5 and p6 updates can require time to complete and there is no visual indication that the command is proceeding.

## Perform Firmware upgrades for BPA on P5/P6

### Define the BPA as a node on the management node

Update the xCAT tables:

Modify the nodelist table. Define the BPA as a node
nodeadd Server-m_tmps_tmp groups=hmc,all

Modify the table nodehm
chtab node="Server-m_tmps_tmp" nodehm.mgt="hmc"

Modify the table nodetype:
chtab node="Server-m_tmps_tmp" nodetype.nodetype="fsp"

Modify the table ppc:
chtab node="Server-m_tmps_tmp" ppc.hcp= hmc01.clusters.com ppc.id=x

Modify the tab vpd:
chtab node=Server-m_tmps_tmp vpd.serial=s_tmp vpd.mtm=m_tmp

Set the account of the HMC(Modify the ppchcp):
chtab hcp=hmc01.clusters.com ppchcp.username=hscroot ppchcp.password=abc123

### Setup SSH connection to HMC
Generate the ssh keys on the xCAT management node and transfer the public key to the HMC to configure the HMC to allow remote ssh connections.
rspconfig hmc01.clusters.com sshcfg=enable

### User rinv to check the firmware level ( see rinv manpage)
rinv Server-m_tmps_tmp firm

### Update the firmware
Download he Microcode update package and associated XML file from the IBM Web site:
        http://www14.software.ibm.com/webapp/set2/firmware/gjsn
Create the /tmp/fw directory, if necessary, and copy the downloaded files to the /tmp/fw directory.

Run the rflash command with the --activate flag to specify the update mode to perform the updates.
rflash Server-m_tmps_tmp -p /tmp/fw --activate disruptive

NOTE:You Need check your update is concurrent or disruptive here!! other commands sample:
rflash Server-m_tmps_tmp -p /tmp/fw --activate concurrent

## Commit currently activated LIC update(copy T to P) for a CEC/BPA on p5/p6

### Check firmware level
Refer to the environment setup in the section 'Firmware upgrade for CEC on P5/P6' to make sure the firmware version is correct.

### Commit the firmware LIC
Run the rflash command with the –commit flag.
rflash Server-m_tmp-SNs_tmp --commit

Notes:
(1)If the noderange is Lpar, the commit steps are the same as the CEC's.
(2) When the –commit or --recover two flags is used, the noderange cannot be BPA . It only can be CEC or LPAR ,and will take effect for both managed systems and power subsystems.