xCAT 2 on AIX
Installing AIX standalone nodes
(using standard NIM rte method)
  Version: 2.1
Date: 10/31/2008

# Installing AIX nodes (using standard NIM rte method)
This “How-To” illustrates how AIX “standalone” machines may be installed using the NIM “rte” method.
The process uses xCAT features to automatically run the necessary NIM commands.
  NIM is an AIX tool that enables a cluster administrator to centrally manage the installation and configuration of AIX and optional software on machines within a networked environment. This document assumes you are somewhat familiar with NIM. For more information about NIM, see the IBM AIX Installation Guide and Reference. (http://www-03.ibm.com/servers/aix/library/index.html)
The process described below is one basic set of steps that may be used to install an AIX standalone node using the NIM “rte” installation method and is not meant to be a comprehensive guide of all the available NIM options.
Before starting this process it is assumed you have completed the following.

- An AIX system has been installed to use as an xCAT management node.
- All relevant base AIX services are configured and running. This includes (but is not limited to) bootp, tftp, NFS, and hostname resolution.
- The cluster network is set up. (The Ethernet network that will be used to perform the network boot of the nodes.)
- xCAT and prerequisite software has been installed on the management node.
- LPARs have already been created using the HMC interfaces.

## Create an operating system image
Use the xCAT mknimimage command to create an xCAT osimage definition as well as the required NIM installation resources.
An xCAT osimage definition is used to keep track of a unique operating system image and how it will be deployed.
In order to use NIM to perform a remote network boot of a cluster node the NIM software must be installed, NIM must be configured, and some basic NIM resources must be created.
The mknimimage will handle all the NIM setup as well as the creation of the xCAT osimage definition. It will not attempt to reinstall or reconfigure NIM if that process has been completed. See the mknimimage man page for additional details.
Note: If you wish to install and configure NIM manually you can run the AIX nim_master_setup command (Ex. “nim_master_setup -a mk_resource=no -a device=<source directory>").
When you run the mknimimage command you must provide a source directory for the required software. For the initial setup this is typically the product media (ex. /dev/cd0) but it could also be the name of an existing “lpp_source” resource.
In this example we need resources for installing a NIM “standalone” type machine using the NIM “rte” install method. (This type and method are the defaults for the mknimimage command but you can specify other values on the command line.)
For example, to create an osimage named “610image” and the required NIM resources you could run the following command.
mknimimage -s /dev/cd0 610image
(Creating the NIM resources could take a while!)
By default the command will create NIM lpp_source, spot, bosinst_data, and resolv_conf resources. You can also specify alternate or additional resources on the command line using the “attr=value” option, (“<nim resource type>=<resource name>”).
For example, if you want to include a NIM installp_bundle resource named mysshbndl you could run the command as follows.
mknimimage -s /dev/cd0 610image installp_bundle= mysshbndl
When the command completes it will display the osimage definition which will contain the names of all the NIM resources that were created. The naming convention for the NIM resources that are created is the osimage name followed by the NIM resource type, (ex. “ 610image_lpp_source”), except for the SPOT name. The default name for the SPOT resource will be the same as the osimage name.
The xCAT osimage definition can be listed using the lsdef command, modified using the chdef command and removed using the rmnimimage command. See the man pages for details.
In some cases you may also want to modify the contents of the NIM resources. For example, you may want to change the bosinst_data file or add to the resolv_conf file etc. For details concerning the NIM resources refer to the NIM documentation.
You can list NIM resource definitions using the AIX lsnim command. For example, if the name of your SPOT resource is "610image" then you could get the details by running:
lsnim -l 610image
To see the actual contents of a NIM resource use "nim -o showres <resource name>". For example, to get a list of the software installed in your SPOT you could run:
        nim -o showres 610image
Note: The mknimimage command will take care of the NIM master installation and configuration automatically, however, you can also do this using the standard AIX support. See the AIX documentation for details on using the nim_master_setup command or the SMIT “eznim” interface.
## Create additional NIM network definitions (optional)
For this example we are assuming that the xCAT management node and the LPARs are all connected to the same network.
However, depending on your specific situation, you may need to create additional NIM network and route definitions.
NIM network definitions represent the networks used in the NIM environment. When the NIM master is configured the network associated with the NIM master is automatically defined. You need to define additional networks only if there are nodes that reside on other local area networks or subnets. If the physical network is changed in any way, the NIM network definitions need to be modified. See the NIM documentation for details on creating additional network and route definitions.
## Define xCAT networks
Create an xCAT network definition for each network that contains cluster nodes. You will need a name for the network and values for the following attributes.
net The network address.
mask The network mask.
gateway The network gateway.

In our example we will assume that all the cluster node management interfaces and the xCAT management node interface are on the same network. You can use the xCAT mkdef command to define the network.

For example:

mkdef -t network -o net1 net=9.114.113.224 mask=255.255.255.224	gateway=9.114.113.254

  Note: The xCAT definition should correspond to the NIM network definition. If multiple cluster subnets are needed then you will need an xCAT and NIM network definition for each one.
## Define the HMC as an xCAT node
The xCAT hardware control support requires that the hardware control point for the nodes also be defined as a cluster node.
The following command will create an xCAT node definition for an HMC with a host name of “hmc01”. The groups, nodetype, mgt, username, and password attributes must be set.
mkdef –t node –o hmc01 groups=”all” nodetype=hmc mgt=hmc	username=hscroot password=abc123
## Discover the LPARs managed by the HMC

This step assumes that the partitions are already created using the standard HMC interfaces.
Use the rscan command to gather the LPAR information. This command can be used to display the LPAR information in several formats and can also write the LPAR information directly to the xCAT database. In this example we will use the “-z” option to create a stanza file that contains the information gathered by rscan as well as some default values that could be used for the node definitions.
To write the stanza format output of rscan to a file called “mystanzafile” run the following command.
rscan –z hmc01 > mystanzafile
This file can then be checked and modified as needed. For example you may need to add a different name for the node definition or add additional attributes and values.
Note: The stanza file will contain stanzas for things other than the LPARs. This information must also be defined in the xCAT database. It is not necessary to modify the non-LPAR stanzas in any way.
The updated stanza file might look something like the following.
Server-9117-MMA-SN10F6F3D:
        objtype=node
        nodetype=fsp
        id=5
        model=9118-575
        serial=02013EB
        hcp=hmc01
        pprofile=
        parent=Server-9458-10099201WM_A
        groups=fsp,all
        mgt=hmc

node01:
        objtype=node
        nodetype=lpar,osi
        id=9
        hcp=hmc01
        pprofile=lpar9
        parent=Server-9117-MMA-SN10F6F3D
        groups=all
        mgt=hmc

node02:
        objtype=node
        nodetype=lpar,osi
        id=7
        hcp=hmc01
        pprofile=lpar6
        parent=Server-9117-MMA-SN10F6F3D
        groups=all
        mgt=hmc

Note: The rscan command supports an option to automatically create node definitions in the xCAT database. To do this the LPAR name gathered by rscan is used as the node name and the command sets several default values. If you use the “-w” option make sure the LPAR name you defined will be the name you want used as your node name.
## Define xCAT cluster nodes
The information gathered by the rscan command can be used to create xCAT node definitions.
Since we have put all the node information in a stanza file we can now pass the contents of the file to the mkdef command to add the definitions to the database.
cat mystanzafile | mkdef –z
You can use the xCAT lsdef command to check the definitions (ex. “lsdef –l node01”). After the node has been defined you can use the chdef command to make any additional updates to the definitions, if needed.

## Define xCAT groups (optional)
There are two basic ways to create xCAT node groups. You can either set the “groups” attribute of the node definition or you can create a group directly.

You can set the “groups” attribute of the node definition when you are defining the node with the mkdef command or you can modify the attribute later using the chdef command. For example, if you want a set of nodes to be added to the group “aixnodes” you could run chdef as follows.
chdef –t node -p –o node01,node02,node03 groups=aixnodes
The “-p” (plus) option specifies that “aixnodes” be added to any existing value for the “groups” attribute.
The second option would be to create a new group definition directly using the mkdef command as follows.
mkdef –t group –o aixnodes members=”node01,node02,node03”
These two options will result in exactly the same definitions and attribute values being created in the xCAT database.
## Set up customization scripts (optional)

xCAT supports the running of user-provided customization scripts on the nodes when they are installed.
To have your script run on the nodes:
1. Put a copy of your script in /install/postscripts on the xCAT management node. (Make sure it is executable.)
2. Set the “postscripts” attribute of the node or group definition to include the comma separated list of the scripts that you want to be executed on the nodes. For example, if you want to have your two scripts called “foo” and “bar” run on node “node01” you could use the chdef command as follows.
chdef -t node -o node01 postscripts=foo,bar
The order of the scripts in the list determines the order in which they will be run.
XCAT also runs some scripts to do default node configuration. You can see what scripts xCAT will run by looking at the “xcatdefaults” entry in the xCAT “postscripts” database table. ( I.e. Run “tabdump postscripts”.). You can change the default setting by using the xCAT chtab or tabedit command.
Note: The customization scripts are run after install to disk but before the first reboot of the system. This corresponds to the NIM “script” resource support. If your script must be run after the first reboot you can define a NIM “fb_script” resource for your script.
## Gather MAC information for the install adapters.
Use the xCAT getmacs command to gather adapter information from the nodes. This command will return the MAC information for each Ethernet adapter available on the target node. The command can be used to either display the results or write the information directly to the database. If there are multiple adapters the first one will be written to the database. The command can also be used to do a ping test on the adapter interfaces to determine which ones could be used to perform the network boot.
For example, to retrieve the MAC address for all the nodes in the group “aixnodes” and write the first adapter MAC to the xCAT database you could issue the following command.
getmacs aixnodes
To display all adapter information but not write anything to the database.
getmacs -d aixnodes
To retrieve the MAC address and do a ping test to determine which adapter MAC to use for the node you could issue the following command. (The ping operation may take a while to complete.)
getmacs -d aixnodes -S 10.14.0.2 -G 10.14.0.2 -C 10.14.0.4
The output would be similar to the following.
# Type Location Code MAC Address Full Path Name Ping Result Device Type
ent U9125.F2A.024C362-V6-C2-T1 fef9dfb7c602 /vdevice/l-lan@30000002 successful virtual
ent U9125.F2A.024C362-V6-C3-T1 fef9dfb7c603 /vdevice/l-lan@30000003 unsuccessful virtual
From this result you can see that “ fef9dfb7c602” should be used for this nodes MAC address.
For more information on using the getmacs command see the man page.
## Create NIM client & group definitions
You can use the xCAT xcat2nim command to automatically create NIM machine and group definitions based on the information contained in the xCAT database. By doing this you synchronize the NIM and xCAT names so that you can use the same target names when running either an xCAT or NIM command.

To create NIM machine definitions you could run the following command.

xcat2nim -t node aixnodes

To create a NIM group definition called “aixnodes” you could run the following command.

xcat2nim –t group –o aixnodes

To check the NIM definitions you could use the NIM lsnim command or the xCAT xcat2nim command. For example, the following command will display the NIM definitions of the nodes: node01, node02, and node03 (from data stored in the NIM database).

xcat2nim -t node -l –o node01-node03
## Initialize the AIX/NIM nodes

You can use the xCAT nimnodeset command to initialize the AIX standalone nodes. This command uses information from the xCAT osimage definition and default values to run the appropriate NIM commands.

For example, to set up all the nodes in the group “aixnodes” to install using the osimage named “610image” you could issue the following command.

nimnodeset -i 610image aixnodes
To verify that you have allocated all the NIM resources that you need you can run the “lsnim –l” command. For example, to check node “node01” you could run the following command.

lsnim -l node01
The nimnodeset command will also set the “profile” attribute in the xCAT node definitions to “610image “. Once this attribute is set you can run the nimnodeset command without the “-i” option.
## Initiate a network boot
Initiate a remote network boot request using the xCAT rnetboot command. For example, to initiate a network boot of all nodes in the group “aixnodes” you could issue the following command.
rnetboot aixnodes
Note: If you receive timeout errors from the rnetboot command, you may need to increase the default 60-second timeout to a larger value by setting ppctimeout in the site table:
chdef -t site -o clustersite ppctimeout=180
## Verify the deployment
As soon as the rnetboot command returns you can open a remote console to monitor the boot progress using the xCAT rcons command. This command requires that you have conserver installed and configured.
To configure conserver:
Set the “cons” attribute of the node definitions to “hmc”.
chdef -t node -o aixnodes cons=hmc
Run the xCAT command.
makeconservercf
Kill the conserver daemon if it is running, and restart it:
conserver &
(You may need to add /opt/freeware/bin and /opt/freeware/sbin to your PATH first).
To start a console:
rcons node01
- You can use the AIX lsnim command to see the state of the NIM installation for a particular node, by running the following command on the NIM master:
  lsnim -l <clientname>
- Retry and troubleshooting tips:
- For p6 lpars, it may be helpful to bring up the HMC web interface in a browser and watch the lpar status and reference codes as the node boots.
- Verify network connections
- If the rnetboot returns “unsuccessful” for a node, verify that bootp and tftp is configured and running properly.
- View /etc/bootptab to make sure an entry exists for the node.
- Verify that the information in /tftpboot/<node>.info is correct.
- Stop and restart inetd:
stopsrc -s inetd
startsrc -s inetd
Stop and restart tftp:
stopsrc -s tftp
startsrc -s tftp
- Verify NFS is running properly and mounts can be performed with this NFS server:
- View /etc/exports for correct mount information.
- Run the showmount and exportfs commands.
- Stop and restart the NFS and related daemons:
stopsrc -g nfs
startsrc -g nfs
Attempt to mount a filesystem from another system on the network.
# Cleanup
The NIM definitions and resources that are created by xCAT commands are not automatically removed. It is therefore up to the system administrator to do some clean up of unused NIM definitions and resources from time to time. (The NIM lpp_source and SPOT resources are quite large.) There are xCAT commands that can be used to assist in this process.

## Removing NIM machine definitions
Use the xCAT xcat2nim command to remove all NIM machine definitions that were created for the specified xCAT nodes. This command will not remove the xCAT node definitions.

For example, to remove the NIM machine definition corresponding to the xCAT node named “node01” you could run the command as follows.

xcat2nim -t node -r node01

The xcat2nim command is intended to make it easier to clean up NIM machine definitions that were created by xCAT. You can also use the AIX nim command directly. See the AIX/NIM documentation for details.

## Removing NIM resources
Use the xCAT rmnimimage command to remove all the NIM resources associated with a given xCAT osimage definition. The command will only remove a NIM resource if it is not allocated to a node. You should always clean up the NIM node definitions before attempting to remove the NIM resources. The command will also remove the xCAT osimage definition that is specified on the command line.
For example, to remove the “610image” osimage definition along with all the associated NIM resources run the following command.
rmnimimage 610image
If necessary, you can also remove the NIM definitions directly by using NIM commands. See the AIX/NIM documentation for details.