xCAT 2 on AIX
Using xCAT Service Nodes with AIX
2010／6／16, PM 02:29:43

# Overview

In an xCAT cluster the single point of control is the xCAT management node. However, in order to provide sufficient scaling and performance for large clusters, it may also be necessary to have additional servers to help handle the deployment and management of the cluster nodes. In an xCAT cluster these additional servers are referred to as service nodes.

For an xCAT on AIX cluster the there is a primary NIM master which is typically on the management node. The service nodes are configured as additional NIM masters. All commands are run on the management node. The xCAT support automatically handles the setup of the low level service nodes and the distribution of the NIM resources. All installation resources for the cluster are managed from the primary NIM master. The NIM resources are automatically replicated on the low level masters when they are needed.

You can set up one or more service nodes in an xCAT cluster. The number you need will depend on many factors including the number of nodes in the cluster, the type of node deployment, the type of network etc. (As a general “rule of thumb” you should plan on having at least 1 service node per 128 cluster nodes.)

A service node may also be used to run user applications in most cases.

An xCAT service node must be installed with xCAT software as well as additional prerequisite software. See the section “Contents of xCATaixSN.bnd and xCATaixSSH.bnd” below for a list of the software that is required for AIX service nodes.

When using service nodes you must switch to a database that supports remote access. As a convenience, version 5.0 of the MySQL database is included in the xcat-mysql-<version>.tar.gz tar file that is available from the xCAT download site. This and other versions of MySQL are also available directly from the MySQL web site. (See http://dev.mysql.com/downloads/mysql/5.1.html#aix)

This document describes the process for setting up AIX service nodes and using them to deploy diskless cluster nodes. The cluster nodes will be System p logical partitions.

AIX service nodes must be diskfull (NIM standalone) systems. Diskless xCAT service nodes are not currently supported for AIX.

In the process described below the service nodes will be deployed using a standard AIX/NIM “rte” network installation. If you are using multiple service nodes you may want to consider creating a “golden” mksysb image that you can use as a common image for all the service nodes. See the xCAT document named “Cloning AIX nodes (using an AIX mksysb image)” for more information on using mksysb images. (http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIXmksysb.pdf)

In this document it is assumed that the cluster nodes will be diskless. The cluster nodes will be deployed using a common diskless image. It is also possible to deploy the cluster nodes using “rte” or “mksysb” type installs.

Before starting this process it is assumed you have configured an xCAT management node by following the process described in the “xCAT2onAIX” overview document. (http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIX.pdf)

The process described below also assumes that System p LPARs for the cluster have already been defined using the standard HMC interfaces. At a minimum you need to define the partitions to use for your diskfull service nodes and at least one diskless partition (per CEC). The additional diskless partitions can be defined later in the process using the xCAT mkvm command if desired.
When defining the LPARs there are a couple things to keep in mind that may help with the rest of the cluster deployment.
1. When configuring an LPAR it would be advisable to use the host name you will want to use for the node as the LPAR name. When you run the xCAT rscan command in the process described below the default host name used for the node definitions will be the LPAR names.
2. It would also be advisable to use an LPAR naming convention that is representative of the cluster organization. For example, you might want to use “sn” in the names of the service node LPARs or “cn” in the cluster node LPARS or some other naming convention that helps keep track of a nodes characteristics etc.

# Additional configuration of the management node
## Switch to the MySQL database
The xCAT support for Service Nodes requires a database with remote access capabilities. The MySQL database is provided for this purpose.

See the “xCAT 2.1 MySQL Setup” document for details on installing, configuring and migrating to MySQL.

http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2.SetupMySQL.pdf

Note: Make sure you add MySQL access for each of your service nodes.
# Install the Service Nodes
## Define the HMCs as xCAT nodes
The xCAT hardware control support requires that the hardware control point for the nodes also be defined as a cluster node.
The following example will create an xCAT node definition for an HMC with a host name of “hmc01”. The groups, nodetype, mgt, username, and password attributes must be set.
mkdef –t node –o hmc01 groups=”all” nodetype=hmc mgt=hmc	username=hscroot password=abc123
## Discover the LPARs managed by the HMCs
This step assumes that the partitions are already created using the standard HMC interfaces.
Use the rscan command to gather the LPAR information. This command can be used to display the LPAR information in several formats and can also write the LPAR information directly to the xCAT database. In this example we will use the “-z” option to create a stanza file that contains the information gathered by rscan as well as some default values that could be used for the node definitions.
To write the stanza format output of rscan to a file called “mystanzafile” run the following command.
rscan –z hmc01 > mystanzafile
The file will contain stanzas for all the LPARs that have been configured as well as some additional information that must also be defined in the xCAT database. It is not necessary to modify the non-LPAR stanzas in any way.
This file can then be checked and modified as needed. For example you may need to add a different name for the node definition or add additional attributes and values.
Since we are using service nodes there are several values that must be set for the node definitions. You can set these values later, after the nodes have been defined, or you can modify the stanzas to include the values now. (If you have many nodes it would be easier to do this later.)
For service nodes:
- Add “service” to the “groups” attribute of all the service nodes.
- The “setupnameserver” attribute of the service nodes must be explicitly set to “yes” or “no”. (Ex. “setupnameserver=no”)
For non-service nodes:
- Add the name of the service node for a node to the node definition. (Ex. “servicenode=xcatSN01”) This is the name of the service node as it is known by the management node.
- Set the “xcatmaster” attribute. This must be the name of the service node as it is known by the node. This may or may not be the same value as the “servicenode “ attribute.
Note: if the “servicenode” and “xcatmaster” values are not set then xCAT will default to use the value of the “master” attribute in the xCAT “site” definition.
The updated stanzas might look something like the following.

cl2sn01:
        objtype=node
        nodetype=lpar,osi
        id=9
        hcp=hmc01
        pprofile=lpar9
        parent=Server-9117-MMA-SN10F6F3D
        groups=all,service
        setupnameserver=no
        mgt=hmc

cl2cn27:
        objtype=node
        nodetype=lpar,osi
        servicenode=cl2sn01 # name of service node as known by the	#management node
        xcatmaster=cl2sn01-en1 # name of the service node as known by the	#node
        id=7
        hcp=hmc01
        pprofile=lpar6
        parent=Server-9117-MMA-SN10F6F3D
        groups=all
        mgt=hmc

Server-9117-MMA-SN10F6F3D:
        objtype=node
        nodetype=fsp
        id=5
        model=9118-575
        serial=02013EB
        hcp=hmc01
        pprofile=
        parent=Server-9458-10099201WM_A
        groups=fsp,all
        mgt=hmc

Note: The rscan command supports an option to automatically create node definitions in the xCAT database. To do this the LPAR name gathered by rscan is used as the node name and the command sets several default values. If you use the “-w” option make sure the LPAR name you defined will be the name you want used as your node name.
## Define xCAT service nodes
The information gathered by the rscan command can be used to create xCAT node definitions.
Since we have put all the node information in a stanza file we can now pass the contents of the file to the mkdef command to add the definitions to the database.
The stanza file will include any LPARs that were already created so it may include nodes other than just the service nodes.
cat mystanzafile | mkdef –z
You can use the xCAT lsdef command to check the definitions (ex. “lsdef –l node01”). After the node has been defined you can use the chdef command to make additional updates to the definitions, if needed.
Make sure the node attributes required for service nodes support are set as mentioned in the previous step. For example to set the required attributes for service node “cl2sn01” you could run the following.
chdef -t node -o cl2sn01 -p groups=service setupnameserver=no
## Add IP addresses and hostnames to /etc/hosts

Make sure all node hostnames are added to /etc/hosts. Refer to the section titled “Add cluster nodes to the /etc/hosts file” in the following document for details. (http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIX.pdf)

## Create a Service Node operating system image

Use the xCAT mknimimage command to create an xCAT osimage definition as well as the required NIM installation resources.
An xCAT osimage definition is used to keep track of a unique operating system image and how it will be deployed.
In order to use NIM to perform a remote network boot of a cluster node the NIM software must be installed, NIM must be configured, and some basic NIM resources must be created.
The mknimimage will handle all the NIM setup as well as the creation of the xCAT osimage definition. It will not attempt to reinstall or reconfigure NIM if that process has already been completed. See the mknimimage man page for additional details.
Note: If you wish to install and configure NIM manually you can run the AIX nim_master_setup command (Ex. “nim_master_setup -a mk_resource=no -a device=<source directory>").
By default, the mknimimage command will create the NIM resources in subdirectories of /install. Some of the NIM resources are quite large (1-2G) so it may be necessary to increase the file size limit.
For example, to set the file size limit to “unlimited” for the user “root” you could run the following command.
/usr/bin/chuser fsize=-1 root
When you run the command you must provide a source for the installable images. This could be the AIX product media, a directory containing the AIX images, or the name of an existing NIM lpp_source resource. You must also provide a name for the osimage you wish to create. This name will be used for the NIM SPOT resource that is created as well as the name of the xCAT osimage definition. The naming convention for the other NIM resources that are created is the osimage name followed by the NIM resource type, (ex. “ 61cosi_lpp_source”).
In this example we need resources for installing a NIM “standalone” type machine using the NIM “rte” install method. (This type and method are the defaults for the mknimimage command but you can specify other values on the command line.)
For example, to create an osimage named “610SNimage” using the images contained in the /myimages directory you could issue the following command.
mknimimage -s /myimages 610SNimage
(Creating the NIM resources could take a while!)
Note: To populate the /myimages directory you could copy the software from the AIX product media using the AIX gencopy command. For example you could run “gencopy -U -X -d /dev/cd0 -t /myimages all".
By default the command will create NIM lpp_source, spot, and bosinst_data resources. You can also specify alternate or additional resources on the command line using the “attr=value” option, (“<nim resource type>=<resource name>”).
For example:
mknimimage -s /dev/cd0 610SNimage resolv_conf=my_resolv_conf
Any additional NIM resources specified on the command line must be previously created using NIM interfaces. (Which means NIM must already have been configured previously. )
Note: Another alternative is to run mknimimage without the additional resources and then simply add them to the xCAT osimage definition later. You can add or change the osimage definition at any time. When you initialize and install the nodes xCAT will use whatever resources are specified in the osimage definition.
When the command completes it will display the osimage definition which will contain the names of all the NIM resources that were created. The naming convention for the NIM resources that are created is the osimage name followed by the NIM resource type, (ex. “ 610SNimage_lpp_source”), except for the SPOT name. The default name for the SPOT resource will be the same as the osimage name.
The xCAT osimage definition can be listed using the lsdef command, modified using the chdef command and removed using the rmnimimage command. See the man pages for details.
In some cases you may also want to modify the contents of the NIM resources. For example, you may want to change the bosinst_data file or add to the resolv_conf file etc. For details concerning the NIM resources refer to the NIM documentation.
You can list NIM resource definitions using the AIX lsnim command. For example, if the name of your SPOT resource is "610SNimage" then you could get the details by running:
lsnim -l 610SNimage
To see the actual contents of a NIM resource use "nim -o showres <resource name>". For example, to get a list of the software installed in your SPOT you could run:
        nim -o showres 610SNimage
Note: The mknimimage command will take care of the NIM installation and configuration automatically, however, you can also do this using the standard AIX support. See the AIX documentation for details on using the nim_master_setup command or the SMIT “eznim” interface.
## Add required service node software
An xCAT AIX service node must also be installed with additional software.
To simplify this process xCAT includes the required xCAT and open source software in the core-aix-<version>.tar.gz and dep-aix-<version>.tar.gz tar files. You will also need the openssl and openssh software that was installed on the management node.
The required software must be copied to the NIM lpp_source that is being used for this OS image. The easiest way to do this is to use the “nim -o update” command.
For example, assume all the required software has been copied and unwrapped in the /tmp/images directory.
To add all the packages to our lpp_source resource, you can run the following:
nim -o update -a packages=all -a source=/tmp/images 610SNimage_lpp_source
The NIM command will find the correct directories and update the lpp_source resource.
To get this additional software installed we need a way to tell NIM to include it. To facilitate this, xCAT provides two AIX installp bundle files. The files are included in the core-aix-<version>.tar.gz file. Starting with xCAT version 2.5 these sample bundle files are installed in “/opt/xcat/share/xcat/installp_bundles”.
To use the bundle files you need to define them as NIM resources and add them to the xCAT osimage definition.
Copy the bundle files ( xCATaixSN.bnd and xCATaixSSH.bnd) to a location where they can be defined as a NIM resource, for example “/install/nim/installp_bundle”.
To define the NIM resources you can run the following commands.
nim -o define -t installp_bundle -a server=master -a location=	/install/nim/installp_bundle/xCATaixSN.bnd xCATaixSN
nim -o define -t installp_bundle -a server=master -a location=	/install/nim/installp_bundle/xCATaixSSH.bnd xCATaixSSH
To add these bundle resources to your xCAT osimage definition run:
chdef -t osimage -o 610SNimage	installp_bundle=”xCATaixSN,xCATaixSSH”
Note: Make sure the xCATaixSN comes first! There is a temporary issue with the AIX openssh installp package that requires that it be done in a separate bundle file that comes after the xCATaixSN bundle (which contains the openssh dependency.).
### Verify the lpp_source contents
At this point you should verify that all the software listed in your bundle files has been copied to your lpp_source directories.

To find the location of the lpp_source directories run the “lsnim -l <lpp_source_name>” command.
lsnim -l 610SNimage_lpp_source
If the location of your lpp_source resource is "/install/nim/lpp_source/610SNimage_lpp_source/" then you would find rpm packages in "/install/nim/lpp_source/610SNimage_lpp_source/RPMS/ppc" and you would find your installp and emgr packages in "/install/nim/lpp_source/610SNimage_lpp_source/installp/ppc".
## Define xCAT networks
Create an xCAT network definition for each network that contains cluster nodes. You will need a name for the network and values for the following attributes.
net The network address.
mask The network mask.
gateway The network gateway.

In our example we will assume that all the cluster node management interfaces and the xCAT management node interface are on the same network. You can use the xCAT mkdef command to define the network.

For example:

mkdef -t network -o net1 net=9.114.0.0 mask=255.255.255.224	gateway=9.114.113.254

Note: The xCAT definition should correspond to the NIM network definition. If multiple cluster subnets are needed then you will need an xCAT and NIM network definition for each one.
## Create additional NIM network definitions (optional)

For the processs described in this document we are assuming that the xCAT management node and the LPARs are all on the same network.
However, depending on your specific situation, you may need to create additional NIM network and route definitions.
NIM network definitions represent the networks used in the NIM environment. When you configure NIM, the primary network associated with the NIM master is automatically defined. You need to define additional networks only if there are nodes that reside on other local area networks or subnets. If the physical network is changed in any way, the NIM network definitions need to be modified.
To create the NIM network definitions corresponding to the xCAT network definitions you can use the xCAT xcat2nim command.
For example, to create the NIM definitions corresponding to the xCAT “clstr_net” network you could run the following command.
xcat2nim -V -t network -o clstr_net

Manual method
The following is an example of how to define a new NIM network using the NIM command line interface.
Step 1
Create a NIM network definition. Assume the NIM name for the new network is “clstr_net”, the network address is “10.0.0.0”, the network mask is “255.0.0.0”, and the default gateway is “10.0.0.247”.
nim -o define -t ent -a net_addr=10.0.0.0 -a snm=255.0.0.0 -a	routing1='default 10.0.0.247' clstr_net
Step 2
Create a new interface entry for the NIM “master” definition. Assume that the next available interface index is “2” and the hostname of the NIM master is “xcataixmn”. This must be the hostname of the management node interface that is connected to the “clstr_net” network.
nim -o change -a if2='clstr_net xcataixmn 0' -a cable_type2=N/A master
Step 3
Create routing information so that NIM knows how to get from one network to the other. Assume the next available routing index is “2”, and the IP address of the NIM master on the “master_net” network is “8.124.37.24”. Assume the IP address on the NIM master on the “clstr_net” network is “ 10.0.0.241”. This command will set the route from “master_net” to “clstr_net” to be “ 10.0.0.241” and it will set the route from “clstr_net” to “master_net” to be “8.124.37.24”.
nim -o change -a routing2='master_net 10.0.0.241 8.124.37.24'	clstr_net
Step 4
Verify the definitions by running the following commands.
lsnim -l master
lsnim -l master_net
lsnim -l clstr_net

See the NIM documentation for details on creating additional network and route definitions. (IBM AIX Installation Guide and Reference. http://www-03.ibm.com/servers/aix/library/index.html)

## Define an xCAT “service” group
If you did not already create the xCAT “service” group when you defined your nodes then you can do it now using the mkdef or chdef command.

There are two basic ways to create xCAT node groups. You can either set the “groups” attribute of the node definition or you can create a group directly.

You can set the “groups” attribute of the node definition when you are defining the node with the mkdef command or you can modify the attribute later using the chdef command. For example, if you want to create the group called “service” with the members sn01 and sn02 you could run chdef as follows.
chdef –t node -p –o sn01,sn02 groups=service
The “-p” option specifies that “service” be added to any existing value for the “groups” attribute.
The second option would be to create a new group definition directly using the mkdef command as follows.
mkdef –t group –o service members=”sn01,sn02”
These two options will result in exactly the same definitions and attribute values being created.
## Include customization scripts
xCAT supports the running of customization scripts on the nodes when they are installed.
This support includes:
- The running of a set of default customization scripts that are required by xCAT.
  You can see what scripts xCAT will run by default by looking at the “xcatdefaults” entry in the xCAT “postscripts” database table. ( I.e. Run “tabdump postscripts”.). You can change the default setting by using the xCAT chtab or tabedit command. The scripts are contained in the /install/postscripts directory on the xCAT management node.
- The optional running of customization scripts provided by xCAT.
  There is a set of xCAT customization scripts provided in the /install/postscripts directory that can be used to perform optional tasks such as additional adapter configuration.
- The optional running of user-provided customization scripts.
To have your script run on the nodes:
1. Put a copy of your script in /install/postscripts on the xCAT management node. (Make sure it is executable.)
2. When using service nodes make sure the postscripts are copied to the /install/postscripts directories on each service node.
3. Set the “postscripts” attribute of the node definition to include the comma separated list of the scripts that you want to be executed on the nodes. The order of the scripts in the list determines the order in which they will be run. For example, if you want to have your two scripts called “foo” and “bar” run on node “node01” you could use the chdef command as follows.
chdef -t node -o node01 -p postscripts=foo,bar
(The “-p” means to add these to whatever is already set.)
Note: The customization scripts are run during the boot process (out of /etc/inittab).
### Add “servicnode” script for service nodes
You must add the “servicenode” script to the postscripts attribute of all the service node definitions. To do this you could modify each node definition individually or you could simply modify the definition of the “service” group.
For example, to have the “servicenode” postscript run on all nodes in the group called “service” you could run the following command.
chdef -p -t group service postscripts=servicenode
### Add NTP setup script (optional)

To have xCAT automatically set up ntp on the cluster nodes you must add the setupntp script to the list of postscripts that are run on the nodes.
To do this you can either modify the “postscripts” attribute for each node individually or you can just modify the definition of a group that all the nodes belong to.
For example, if all your nodes belong to the group “compute” then you could add setupntp to the group definition by running the following command.
chdef -p -t group -o compute postscripts=setupntp
Note: In hierarchy cluster, the ntpserver for the compute nodes will be pointed to the their service nodes, so if you want to set up ntp on the compute nodes, make sure the ntp server is set up correctly on the service nodes, the setupntp postscript can set up both the ntp client and the ntp server.
### Add secondary adapter configuration script

It is possible to have additional adapter interfaces automatically configured when the nodes are booted. XCAT provides sample configuration scripts for both Ethernet and IB adapters. These scripts can be used as-is or they can be modified to suit you particular environment. The Ethernet sample is /install/postscript/configeth. When you have the configuration script that you want you can add it to the “postscripts” attribute as mentioned above. Make sure your script is in the /install/postscripts directory and that it is executable.

If you wish to configure IB interfaces please refer to: “xCAT 2 InfiniBand Support” http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2IBsupport.pdf

## Gather MAC information for the install adapters.
Use the xCAT getmacs command to gather adapter information from the nodes. This command will return the MAC information for each Ethernet adapter available on the target node. The command can be used to either display the results or write the information directly to the database. If there are multiple adapters the first one will be written to the database.
The command can also be used to do a ping test on the adapter interfaces to determine which ones could be used to perform the network boot. In this case the first adapter that can be successfully used to ping the server will be written to the database.
Before running getmacs you must first run the makeconservercf command. You need to run makeconservercf any time you add new nodes to the cluster.
makeconservercf
Shut down all the nodes that you will be querying for MAC addresses.
rpower aixnodes off
To retrieve the MAC address for all the nodes in the group “aixnodes” and write the first adapter MAC to the xCAT database you could issue the following command.
getmacs aixnodes
To display all adapter information but not write anything to the database.
getmacs -d aixnodes
To retrieve the MAC address and do a ping test to determine which adapter MAC to use for the node you could issue the following command. (The ping operation may take a while to complete.)
getmacs -d aixnodes -S 10.14.0.2 -G 10.14.0.2 -C 10.14.0.4
The output would be similar to the following.
# Type Location Code MAC Address Full Path Name Ping Result Device Type
ent U9125.F2A.024C362-V6-C2-T1 fef9dfb7c602 /vdevice/l-lan@30000002 successful virtual
ent U9125.F2A.024C362-V6-C3-T1 fef9dfb7c603 /vdevice/l-lan@30000003 unsuccessful virtual
From this result you can see that “ fef9dfb7c602” should be used for this nodes MAC address.
For more information on using the getmacs command see the man page.
## Create NIM client & group definitions
You can use the xCAT xcat2nim command to automatically create NIM machine and group definitions based on the information contained in the xCAT database. By doing this you synchronize the NIM and xCAT names so that you can use the same target names when running either an xCAT or NIM command.

To create NIM machine definitions for your service nodes you could run the following command.

xcat2nim -t node service

To create NIM group definition for the group “service” you could run the following command.

xcat2nim –t group –o service

To check the NIM definitions you could use the NIM lsnim command or the xCAT xcat2nim command. For example, the following command will display the NIM definitions of the nodes contained in the xCAT group called “service”, (from data stored in the NIM database).

xcat2nim -t node -l service
## Initialize the AIX/NIM nodes

You can use the xCAT nimnodeset command to initialize the AIX standalone nodes. This command uses information from the xCAT osimage definition and default values to run the appropriate NIM commands.

For example, to set up all the nodes in the group “service” to install using the osimage named “610SNimage” you could issue the following command.

nimnodeset -i 610SNimage service
To verify that you have allocated all the NIM resources that you need you can run the “lsnim –l” command. For example, to check the node “clstrn01” you could run the following command.

lsnim -l clstrn01
The command will also set the “profile” attribute in the xCAT node definitions to “610SNimage “. Once this attribute is set you can run the nimnodeset command without the “-i” option.
Note: To verify that NIM has properly initialized the nodes you can also check the contents of the /etc/bootptab or /var/lib/dhcp/db/dhcpd.leases, /etc/exports, and the node “info” file in the /tftpboot directory.

## Open a remote console (optional)
You can open a remote console to monitor the boot progress using the xCAT rcons command. This command requires that you have conserver installed and configured.
If you wish to monitor a network installation you must run rcons before initiating a network boot.
To configure conserver run:
makeconservercf
To start a console:
rcons node01
Note: You must always run makeconservercf after you define new cluster nodes.
## Initiate a network boot
Initiate a remote network boot request using the xCAT rnetboot command. For example, to initiate a network boot of all nodes in the group “service” you could issue the following command.
rnetboot service
Note: If you receive timeout errors from the rnetboot command, you may need to increase the default 60-second timeout to a larger value by setting ppctimeout in the site table:
chdef -t site -o clustersite ppctimeout=180
## Verify the deployment
- If you opened a remote console using rcons you can watch the progress of the installation.
- For p6 lpars, it may be helpful to bring up the HMC web interface in a browser and watch the lpar status and reference codes as the node boots.
- You can use the AIX lsnim command to see the state of the NIM installation for a particular node, by running the following command on the NIM master:
  lsnim -l <clientname>
- When the node is booted you can log in and check if it is configured properly. For example, is the password set?, is the timezone set?, can you xdsh to the node etc.
### Retry and troubleshooting tips:
If a node did not boot up:
- Verify network connections. Try a ping test using the HMC console.
- For bootp, check /etc/bootptab to make sure an entry exists for the node.
  For dhcp, check /var/lib/dhcp/db/dhcpd.leases to make sure an entry exists for the node
- Verify that the information in /tftpboot/<node>.info is correct.
- Stop and restart inetd:
stopsrc -s inetd
startsrc -s inetd
- Stop and restart tftp:
stopsrc -s tftpd
startsrc -s tftpd
Verify NFS is running properly and mounts can be performed with this NFS server:
- View /etc/exports for correct mount information.
- Run the showmount and exportfs commands.
- Stop and restart the NFS and related daemons:
stopsrc -g nfs
startsrc -g nfs
- Attempt to mount a filesystem from another system on the network.
- You may need to reset the NIM client definition and start over.
nim -Fo reset node01
nim -o deallocate -a subclass=all node01

- If the node booted but one or more customization scripts did not run correctly:
- You can check the /var/log/messages file on the management node and the var/log/xcat/xcat.log file on the node (if it is up) to see if any error messages were produced during the installation.
- Restart the xcatd daemon (xcatstop & xcatstart (xCAT2.4 restartxcatd)) and then re-run the customization scripts either manually or by using updatenode.
## Configure additional adapters on the service nodes (optional)

If additional adapter configuration is required on the service nodes you could either use the xdsh command to run the appropriate AIX commands on the nodes or you may want to use the updatenode command to run a configuration script on the nodes.

XCAT provides sample adapter interface configuration scripts for Ethernet and IB. The Ethernet sample is /install/postscripts/configeth. It illustrate how to use a specific naming convention to automatically configure interfaces on the node. You can modify this script for you environment and then run it on the node using updatenode. First copy your script to the /install/postscripts directory and make sure it is executable. Then run a command similar to the following.

updatenode clstrn01 myconfigeth

If you wish to configure IB interfaces please refer to: “xCAT 2 InfiniBand Support” http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2IBsupport.pdf
## Verify Service Node configuration
During the node boot up there are several xCAT post scripts that are run that will configure the node as an xCAT service node. It is advisable to check the service nodes to make sure they are configured correctly before proceeding.

There are several things that can be done to verify that the service nodes have been configured correctly.

1. Check if NIM has been installed and configured by running “lsnim” or some other basic NIM command on the service node.
2. Check to see if all the additional software has been installed. For example, Run “rpm -qa” to see if the xCAT and dependency software is installed.
3. Try running some xCAT commands such as “lsdef -a”to see if the xcatd daemon is running and if data can be retrieved from the xCAT database on the management node.
4. If using SSH for your remote shell try to ssh to the service nodes from the management node.
5. Check the system services, as mentioned earlier in this document, to make sure the service node can respond to a network boot request.

# Install the cluster nodes
## Create a diskless image
In order to boot a diskless AIX node using xCAT and NIM you must create an xCAT osimage definition as well as several NIM resources.
You can use the xCAT mknimimage command to automate this process.
There are several NIM resources that must be created in order to deploy a diskless node. The main resource is the NIM SPOT (Shared Product Object Tree). An AIX diskless image is essentially a SPOT. It provides a /usr file system for diskless nodes and a root directory whose contents will be used for the initial diskless nodes root directory. It also provides network boot support.
When you run the command you must provide a source for the installable images. This could be the AIX product media, a directory containing the AIX images, or the name of an existing NIM lpp_source resource. You must also provide a name for the osimage you wish to create. This name will be used for the NIM SPOT resource that is created as well as the name of the xCAT osimage definition. The naming convention for the other NIM resources that are created is the osimage name followed by the NIM resource type, (ex. “ 61cosi_lpp_source”).
Stateful or stateless?
You can choose to have your diskless nodes be either “stateful” or “stateless”. If you want a “stateful” node you must use a NIM “root” resource. If you want a “stateless” node you must use a NIM “shared_root” resource.
A “stateful” diskless node preserves its state in individual mounted root filesystems. When the node is shut down and rebooted, any information that was written to a root filesystem will be available
A “stateless “ diskless node uses a mounted root filesystem that is shared with other nodes. When it writes to the root directory the information is actually written to memory. If the node is shut down and rebooted any data that was written is lost. Any node-specific information must be re-established when the node is booted.
The advantage of stateless nodes is that there is much less network traffic and fewer resources used which is especially important in a large cluster environment.
For more information regarding the NIM “root” and “shared_root” resource refer to the NIM documentation.
If you wish to set up stateless cluster nodes you must use the “-r” option when you run the mknimimage command. The default behavior would be to set up stateful nodes.
For example, to create a stateless-diskless osimage called “61cosi” using the software contained in the /myimages directory you could issue the following command.
mknimimage -r -t diskless -s /myimages 61cosi
(Note that this operation could take a while to complete!)
Caution: Do not interrupt (kill) a NIM process while it is creating a SPOT resource.
Starting with xCAT version 2.5 you can also use the “-D” option to specify that a dump resource should be created. See the section called “ISCSI dump support” in the following document for more information on the diskless ISCSI dump support. ( http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIXDiskless.pdf)
Note: To populate the /myimages directory you could copy the software from the AIX product media using the AIX gencopy command. For example you could run “gencopy -U -X -d /dev/cd0 -t /myimages all".
The mknimimage command will display a summary of what was created when it completes. For example:
Object name: 61cosi
    imagetype=NIM
    lpp_source=61cosi_lpp_source
    nimtype=diskless
    osname=AIX
    paging=61cosi_paging
    shared_root=61cosi_shared_root
    spot=61cosi
The NIM resources will be created in a subdirectory of /install/nim by default. You can use the “-l” option to specify a different location.
You can also specify alternate or additional resources on the command line using the “attr=value” option, (“<nim resource type>=<resource name>”). For example, if you want to include a “resolv_conf” resource named “61cosi_resolv_conf” you could run the command as follows.
mknimimage -t diskless -s /dev/cd0 61cosi resolv_conf=61cosi_resolv_conf
Any additional NIM resources specified on the command line must be previously created using NIM interfaces. (Which means NIM must already have been configured previously. )
Note: Another alternative is to run mknimimage without the additional resources and then simply add them to the xCAT osimage definition later. You can add or change the osimage definition at any time. When you initialize and install the nodes xCAT will use whatever resources are specified in the osimage definition.
The xCAT osimage definition can be listed using the lsdef command, modified using the chdef command and removed using the rmnimimage command. See the man pages for details.
To get details for the NIM resource definitions use the AIX lsnim command. For example, if the name of your SPOT resource is "61cosi" then you could get the details by running:
lsnim -l 61cosi
To see the actual contents of a NIM resource use "nim -o showres <resource name>". For example, to get a list of the software installed in your SPOT you could run:
        nim -o showres 61cosi
## Update the image (SPOT)
  The SPOT created in the previous step should be considered the basic minimal diskless AIX operating system image. It does not contain all the software that would normally be installed as part of AIX, if you were installing a standalone system from the AIX product media. (The “nim -o showres ...” command mentioned above will display what software is contained in the SPOT.)
You must install any additional software you need and make any customizations to the image before you boot the nodes.
For more information on updating a diskless image see the document called “Updating AIX cluster nodes” (http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIXUpdates.pdf)
### Update options
There are basically three types of updates you can do to a SPOT.
#### Add or update software
The SPOT created in the previous step should be considered the basic minimal diskless AIX operating system image. It does not contain all the software that would normally be installed as part of AIX, if you were installing a standalone system from the AIX product media. (The “nim -o showres ...” command mentioned above will display what software is contained in the SPOT.)
You can use the mknimimage “-u” option to update software in the diskless image (SPOT).
To do this you can update your xCAT osimage definition with any “installp_bundles”, “otherpkgs” you wish to use and then run the mknimimage -u command.
Use the chdef command to update the osimage definition. For example:
chdef -t osimage -o 61cosi installp_bundle=”hpcbnd,labbnd”
Once the osimage definition is updated you can run mknimimage.
mknimimage -u 61cosi
Note: You can also specify “installp_bundle” and “otherpkgs” on the command line. However in this case you wouldn't have a record of what software was added to the SPOT.
#### Update system configuration files.

You can also add other configuration files such as /etc/passwd etc. These files will then be available to every node that boots with this image.
This can be done manually or by setting the “synclists” attribute of the osimage definition to point to a synclists file. This file contains a list of configuration files etc. that you wish to have copied into the SPOT.
For more information on using the synchronization file function see the document called “How to sync files in xCAT” ( http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2SyncFilesHowTo.pdf )
Use the chdef command to update the osimage definition. For example:
chdef -t osimage -o 61cosi synclists=”/u/test/mysyncfiles”
Once the osimage definition is updated you can run mknimimage.
mknimimage -u 61cosi
Note: You can do BOTH the software updates and configuration file updates at the same time with one call to mknimimage.

#### Run commands in the SPOT using chroot.
Starting with xCAT 2.5 and AIX 6.1.6 the xcatchroot command can be used to modify the SPOT using the chroot command.
The xcatchroot command will take care of any of the required setup so that the command you provide will be able to run in the spot chroot environment. It will also mount the lpp_source resource listed in the osimage definition so that you can access additional software that you may wish to install.
For example, to set the root password to "cluster" in the spot so that when the diskless node boots it will have a root password set you could run a command similar to the following.
xcatchroot -i 61cosi "/usr/bin/echo root:cluster | /usr/bin/chpasswd -c"
See the xcatchroot man page for more details.
Caution:
Be very careful when using chroot on a SPOT. It is easy to get the SPOT into an unusable state! It may be adviseable to make a copy of the SPOT before you try to run any commands that have an uncertain outcome.
When you are done updating a NIM spot resource you should always run the NIM check operation on the spot.
nim -Fo check 61cosi
For more information on updating a diskless image see the document called “Updating AIX cluster nodes” (http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIXUpdates.pdf)
See the section titled “Updating diskless nodes”
### Adding required software
You will have to install openssl and openssh along with several additional requisite software packages.
To help facilitate this task xCAT ships two sample AIX installp_bundle files. They are called xCATaixSSL.bnd and xCATaixSSH.bnd, and they are included in the xCAT tar file. (Starting with xCAT version 2.5 these sample bundle files will be installed in /opt/xcat/share/xcat/installp_bundles.)
The basic process is:
- Copy the required software to the lpp_source resource that you used to create your SPOT.
- Install the software in the SPOT.
#### Copy the software.
You will need to update the SPOT with the openssl and openssh filesets as well as some prerequisite RPM packages that were included in the xCAT dependency tar file. The required filesets and rpms are listed in the xCATaixSSH.bnd and xCATaixSSL.bnd files.
The required software must be copied to the NIM lpp_source resource that is being used for this OS image. The easiest way to do this is to use the “nim -o update” command.
For example, assume all the required software has been copied and unwrapped in the /tmp/images directory and that the name of the NIM lpp_source resource is “61cosi_lpp_source”.
For example:
nim -o update -a packages=all -a source=/tmp/images	61cosi_lpp_source
The NIM command will find the correct directories and update the lpp_source resource.
#### Install the software into the SPOT.
You can install and update software in a NIM SPOT resource by using NIM commands directly or you can use the xCAT mknimimage command.
If you wish to use the NIM support directly you can check the NIM documentation for information on the NIM “cust” and “maint” operations.
In this example the xCAT mknimimage command will be used.
To specify the software to install you can create two NIM installp_bundle resources using the bundle files that are shipped with xCAT.
To use the bundle files you must first define them as NIM resources.
Copy the bundle files ( xCATaixSSL.bnd and xCATaixSSH.bnd) to a location where they can be defined as a NIM resource, for example “/install/nim/installp_bundle”.
To define the NIM resources you can run the following commands.
nim -o define -t installp_bundle -a server=master -a location=	/install/nim/installp_bundle/xCATaixSSL.bnd xCATaixSSL
nim -o define -t installp_bundle -a server=master -a location=	/install/nim/installp_bundle/xCATaixSSH.bnd xCATaixSSH
Add the installp_bundle resource names to the xCAT osimage definition. (Make sure the SSL bundle is first!)
chdef -t osimage -o 61cosi	installp_bundle=”xCATaixSSL,xCATaixSSH”

Verify that all the software that you wish to install has been copied to the appropriate NIM lpp_source directory. To do this you can check the “otherpkgs” attribute of the osimage definition and the contents of any “installp_bundle” resources that are specified.
Run the mknimimage command to update the SPOT using the information saved in the xCAT "61cosi" osimage definition.
mknimimage -u 61cosi
See the mknimimage man page for more options that are available for updating diskless images (SPOT resources).
Note: You cannot update a SPOT that is currently allocated. To check to see if the SPOT is allocated you could run the following command.
lsnim -l <spot name>
## Define xCAT networks
Create a network definition for each network that contains cluster nodes. You will need a name for the network and values for the following attributes.
net The network address.
mask The network mask.
gateway The network gateway.

This “How-To” assumes that all the cluster node management interfaces and the xCAT management node interface are on the same network. You can use the xCAT mkdef command to define the network.

For example:

mkdef -t network -o net1 net=9.114.113.224 mask=255.255.255.224	gateway=9.114.113.254
## Define the LPARs currently managed by the HMC
This step assumes that LPARs were already created using the standard HMC interfaces.
Use the xCAT rscan command to gather the LPAR information. In this example we will use the “-z” option to create a stanza file that contains the information gathered by rscan as well as some default values that could be used for the node definitions.
To write the stanza format output of rscan to a file called “mystanzafile” run the following command.
rscan –z hmc01 > mystanzafile
This file can then be checked and modified as needed. For example you may need to add a different name for the node definition or add additional attributes and values etc.
Note: The stanza file will contain stanzas for objects other than the LPARs. This information must also be defined in the xCAT database. It is not necessary to modify the non-LPAR stanzas in any way
The information gathered by the rscan command can be used to create xCAT node definitions.
Since we have put all the node information in a stanza file we can now pass the contents of the file to the mkdef command to add the definitions to the database.
cat mystanzafile | mkdef –z
You can use the xCAT lsdef command to check the definitions (ex. “lsdef –l node01”). After the node has been defined you can use the chdef command to make any additional updates to the definitions, if needed.
## Create and define additional logical partitions (optional)

You can use the xCAT mkvm command to create additional logical partitions for diskless nodes in some cases.

This command can be used to create new partitions based on an existing partition or it can replicate the partitions from a source CEC to a destination CEC.

The first form of the mkvm command creates new partition(s) with the same profile/resources as the partition specified on the command line. The starting numeric partition number and the noderange for the newly created partitions must also be provided. The LHEA port numbers and the HCA index numbers will be automatically increased if they are defined in the source partition.

The second form of this command duplicates all the partitions from the specified source CEC to the destination CEC. The source and destination CECs can be managed by different HMCs.

The nodes in the noderange must already be defined in the xCAT database. The “mgt” attribute of the node definitions must be set to “hmc”.

For example, to create a set of new nodes. (The “groups” attribute is required.)

mkdef -t node -o clstrn04-clstrn10 groups=all,aixnodes mgt=hmc

To create several new partitions based on the partition for node clstrn01.

mkvm -V clstn01 -i 4 -n clstrn04-clstrn10

See the mkvm man page for more details.
## Gather MAC information for the node boot adapters.
Use the xCAT getmacs command to gather adapter information from the nodes. This command will return the MAC information for each Ethernet adapter available on the target node. The command can be used to either display the results or write the information directly to the database. If there are multiple adapters the first one will be written to the database and used as the install adapter for that node.
The command can also be used to do a ping test on the adapter interfaces to determine which ones could be used to perform the network boot. In this case the first adapter that can be successfully used to ping the server will be written to the database.
Before running getmacs you must first run the makeconservercf command. You need to run makeconservercf any time you add new nodes to the cluster.
makeconservercf
Shut down all the nodes that you will be querying for MAC addresses.
rpower aixnodes off
To retrieve the MAC address for all the nodes in the group “aixnodes” and write the first adapter MAC to the xCAT database you could issue the following command.
getmacs aixnodes
To display all adapter information but not write anything to the database.
getmacs -d aixnodes
To retrieve the MAC address and do a ping test to determine which adapter MAC to use for the node you could issue the following command. (The ping operation may take a while to complete.)
getmacs -d aixnodes -S 10.14.0.2 -G 10.14.0.2 -C 10.14.0.4
The output would be similar to the following.
# Type Location Code MAC Address Full Path Name Ping Result Device Type
ent U9125.F2A.024C362-V6-C2-T1 fef9dfb7c602 /vdevice/l-lan@30000002 successful virtual
ent U9125.F2A.024C362-V6-C3-T1 fef9dfb7c603 /vdevice/l-lan@30000003 unsuccessful virtual
From this result you can see that “ fef9dfb7c602” should be used for this nodes MAC address.
For more information on using the getmacs command see the man page.
To add the MAC value to the node definition you can use the chdef command. For example:
chdef -t node node01 mac=fef9dfb7c603
## Define xCAT groups (optional)
XCAT supports both static and dynamic node groups. See the section titled “xCAT node group support” in the “xCAT2 Top Doc” document for details on using xCAT groups. ( http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2top.pdf)

Note: The dynamic node group support is only available in xCAT 2.3 and beyond.
## Add IP addresses and hostnames to /etc/hosts

Make sure all node hostnames are added to /etc/hosts. Refer to the section titled “Add cluster nodes to the /etc/hosts file” in the following document for details. (http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIX.pdf )
## Verify the node definitions
Verify that the node definitions include the required information.
To get a listing of the node definition you can use the lsdef command. For example to display the definitions of all nodes in the group “aixnodes” you could run the following command.
lsdef -t node -l -o aixnodes
The output for one diskless node might look something like the following:
Object name: clstrn02
    cons=hmc
    groups=lpar,all
    servicenode=clstrSN1
    xcamaster=clstrSN1-en1
    hcp=clstrhmc01
    hostnames=clstrn02.mycluster.com
    id=2
    ip=10.1.3.2
    mac=001a64f9bfc9
    mgt=hmc
    nodetype=lpar,osi
    os=AIX
    parent=clstrf1fsp03-9125-F2A-SN024C352
    pprofile=compute
Most of these attributes should have been filled in automatically by xCAT.
Note: xCAT supports many different cluster environments and the attributes that may be required in a node definition will vary. For diskless nodes using a servicenode, the node definition should include at least the attributes listed in the above example.
Make sure “servicenode” is set to the name of the service node as known by the management node and “xcatmaster” is set to the name of the service node as known by the node.
To modify the node definitions you can use the chdef command.
For example to set the xcatmaster attribute for node “clstrn01” you could run the following.
chdef -t node -o clstrn01 xcatmaster=clstrSN1-en1
## Set up post boot scripts (optional)
xCAT supports the running of customization scripts on the nodes when they are installed. For diskless nodes these scripts are run when the /etc/inittab file is processed during the node boot up.
This support includes:
- The running of a set of default customization scripts that are required by xCAT.
  You can see what scripts xCAT will run by default by looking at the “xcatdefaults” entry in the xCAT “postscripts” database table. ( I.e. Run “tabdump postscripts”.). You can change the default setting by using the xCAT chtab or tabedit command. The scripts are contained in the /install/postscripts directory on the xCAT management node.
- The optional running of customization scripts provided by xCAT.
  There is a set of xCAT customization scripts provided in the /install/postscripts directory that can be used to perform optional tasks such as additional adapter configuration. (See the “configiba” script for example.)
- The optional running of user-provided customization scripts.
To have your script run on the nodes:
1. Put a copy of your script in /install/postscripts on the xCAT management node. (Make sure it is executable.)
2. When using service nodes make sure the postscripts are copied to the /install/postscripts directories on each service node.
3. Set the “postscripts” attribute of the node definition to include the comma separated list of the scripts that you want to be executed on the nodes. The order of the scripts in the list determines the order in which they will be run. For example, if you want to have your two scripts called “foo” and “bar” run on node “node01” you could use the chdef command as follows.
chdef -t node -o node01 -p postscripts=foo,bar
(The “-p” means to add these to whatever is already set.)
Note: The customization scripts are run during the boot process (out of /etc/inittab).
## Initialize the AIX/NIM diskless nodes

You can set up NIM to support a diskless boot of nodes by using the xCAT mkdsklsnode command. This command uses information from the xCAT database and default values to run the appropriate NIM commands.

For example, to set up all the nodes in the group “aixnodes” to boot using the SPOT (COSI) named “61cosi” you could issue the following command.

mkdsklsnode -i 61cosi aixnodes

  The command will define and initialize the NIM machines. It will also set the “profile” attribute in the xCAT node definitions to “61cosi “.
To verify that NIM has allocated the required resources for a node and that the node is ready for a network boot you can run the “lsnim –l” command. For example, to check node “node01” you could run the following command.
lsnim -l node01
Note:
The NIM initialization of multiple nodes is done sequentially and takes approximately three minutes per node to complete. If you are planning to initialize multiple nodes you should plan accordingly. The NIM development team is currently working on a solution for this scaling issue.
### Verifying the node initialization before booting (optional)
Once the mkdsklsnode command completes you can log on to the service node and verify that it has been configured correctly.
- The /etc/bootptab or /var/lib/dhcp/db/dhcpd.leases, /etc/exports files.
- The node info file in the /tftpboot directory.
- The NIM node definition for the node.
## Open a remote console (optional)
You can open a remote console to monitor the boot progress using the xCAT rcons command. This command requires that you have conserver installed and configured.
If you wish to monitor a network installation you must run rcons before initiating a network boot.
To configure conserver run:
makeconservercf
To start a console:
rcons node01
Note: You must always run makeconservercf after you define new cluster nodes.
## Initiate a network boot
Initiate a remote network boot request using the xCAT rnetboot command. For example, to initiate a network boot of all nodes in the group “aixnodes” you could issue the following command.
rnetboot aixnodes
Note: If you receive timeout errors from the rnetboot command, you may need to increase the default 60-second timeout to a larger value by setting ppctimeout in the site table:
chdef -t site -o clustersite ppctimeout=180
## Verify the deployment
Retry and troubleshooting tips:
- For p6 lpars, it may be helpful to bring up the HMC web interface in a browser and watch the lpar status and reference codes as the node boots.
- Verify network connections
- If the rnetboot returns “unsuccessful” for a node, verify that bootp and tftp is configured and running properly on the .
- For bootp, view /etc/bootptab to make sure an entry exists for the node.
  For dhcp, view /var/lib/dhcp/db/dhcpd.leases to make sure an entry exists for the node.
- Verify that the information in /tftpboot/<node>.info is correct.
- Stop and restart inetd:
stopsrc -s inetd
startsrc -s inetd
Stop and restart tftp:
stopsrc -s tftp
startsrc -s tftp
- Verify NFS is running properly and mounts can be performed with this NFS server:
- View /etc/exports for correct mount information.
- Run the showmount and exportfs commands.
- Stop and restart the NFS and related daemons:
stopsrc -g nfs
startsrc -g nfs
Attempt to mount a file system from another system on the network.
If that doesn't work, you may need to re-initialize the diskless node and start over. You can use the rmdsklsnode command to uninitialize an AIX diskless node. This will deallocate and remove the NIM definition but it will not remove the xCAT node definition.
# Cleanup
The NIM definitions and resources that are created by xCAT commands are not automatically removed. It is therefore up to the system administrator to do some clean up of unused NIM definitions and resources from time to time. (The NIM lpp_source and SPOT resources are quite large.) There are xCAT commands that can be used to assist in this process.

## Removing NIM machine definitions
Use the xCAT rmdsklsnode command to remove all the NIM diskless machine definitions that were created for the specified xCAT nodes. This command will not remove the xCAT node definitions.

For example, to remove the NIM machine definition corresponding to the xCAT diskless node named “node01” you could run the command as follows.

rmdsklsnode node01

Use the xCAT xcat2nim command to remove all the NIM standalone machine definitions that were created for the specified xCAT nodes. This command will not remove the xCAT node definitions.

For example, to remove the NIM machine definition corresponding to the xCAT node named “node01” you could run the command as follows.

xcat2nim -t node -r node01

The xcat2nim and rmdsklsnode command are intended to make it easier to clean up NIM machine definitions that were created by xCAT. You can also use the AIX nim command directly. See the AIX/NIM documentation for details.

## Removing NIM resources
Use the xCAT rmnimimage command to remove all the NIM resources associated with a given xCAT osimage definition. The command will only remove a NIM resource if it is not allocated to a node. You should always clean up the NIM node definitions before attempting to remove the NIM resources. The command will also remove the xCAT osimage definition that is specified on the command line.
For example, to remove the “610image” osimage definition along with all the associated NIM resources run the following command.
rmnimimage 610image
If necessary, you can also remove the NIM definitions directly by using NIM commands. See the AIX/NIM documentation for details.