xCAT 2 cookbook for pLinux on IBM Power Series

Date: 02/20/2009

Contents

# Introduction
This cookbook introduces how to use the xCAT2 to install Linux on the IBM power series machines.
The power series machines have the following characteristics:
1. May have multiple LPARs (an LPAR will be the target machine to install an operating system image on, i.e. the LPAR will be the compute node);
2. The Ethernet card and SCSI partition can be virtual devices;
3. An HMC or IVM is used for the HCP (hardware control point)

xCAT supports two types of installations for compute nodes: Diskfull installation (Statefull) and Diskless (Stateless). xCAT also supports hierarchical management clusters where one or more service nodes are used to handle the installation and management of compute nodes. This cookbook will not cover hierarchy.
Based on the two types of installation, the following installation scenarios will be described in this document:
1. Install a stateful compute node
2. Install a stateless compute node

To provide easier understanding of the installation steps, this cookbook provides examples using the following test environment:

The management node:
Arch: an LPAR on a p5/p6 machine
OS: Red Hat 5.2
Hostname: pmanagenode
IP: 192.168.0.1
HCP: HMC

The compute node:
Arch: an LPAR on a p5/p6 machine
OS: Red Hat 5.2
Hostname: pnode1
IP: 192.168.0.10
HCP: HMC

xCAT version:
xCAT-2.1+

# Install the Management node
## Install xCAT 2 on the Management node
Before preceding to setup your pLlinux Cluster, you should first read xCATtop for information on downloading and installing xCAT on your Management Node.
# Setup the Management Node for node installs
## Create a YUM repository for the RHEL node installs
### Copy the iso of the Operating System which this MN running.
You can copy it from internal source server or download it from Internet

mkdir /iso
copy RHEL5.2-Server-20080430.0-ppc-DVD.iso to /iso/
### Mount the content of the iso to a dir

mkdir /iso/1
cd /iso
mount -o loop RHEL5.2-Server-20080430.0-ppc-DVD.iso 1
### Create a yum repository file for OS image
cd /etc/yum.repos.d
Create the /etc/yum.repos.d/rhel-Server.repo:
[rhe-5-server]
name=RHEL 5 SERVER packages
baseurl=file:///iso/1/Server
enabled=1
gpgcheck=0
### Create a zypper repository for SLES
Add the repository using “zypper” command:
zypper ar file:///iso/1 sles11

if you are creating a SLES10.2 repository
   zypper sa file:///iso/1 sles10
# Setup the management node
## Workaround the atftpd issue with p5
The tftp client in the open firmware of p5 is only compatible with tftp-server instead of atftpd which is required by xCAT2. So we have to remove the atftpd first and then install the tftp-server. This is not required for p6 or later.
### Remove atftp (p5 ONLY)
service tftpd stop
rpm --nodeps -e atftp
### Install the tftp server needed by xCAT, and restart it (p5 ONLY)
For RHEL:
yum install tftp-server.ppc
Notes: make sure the entry "disable=no" in the /etc/xinetd.d/tftp.
service xinetd restart
For SLES:
zypper install tftp-server.ppc
## Setup common attributes for xCAT in the database
### Modify the table ppchcp (Set the default account of the HMC)
chtab hcp=hmc.cluster.net ppchcp.username=hscroot ppchcp.password=abc123
### Modify table passwd (Set the default account of the installed node)
chtab key=system passwd.key=system passwd.username=root passwd.password=cluster
## Define nodes in the Database
The definition of a node is stored in several tables of the xCAT database. There are two ways to define a node and add records in tables:
You can use the chdef, mkdef command and add them manually or use the rscan command to collect the data and use a stanza file.
We will use rscan command to get the attributes of the node and save the attributes into a stanza file. The stanza file can be used to update the database. You can then use the commands (mkdef, chdef, lsdef, and rmdef) to display or edit the information that was created in the database.

EXAMPLE:
We want to install a node with following attributes.
Hostname: pnode1
IP: 192.168.0.10
Arch: ppc64 (An Lpar of power5); machine name: Server-9117-MMA-SNxxxx; Lpar ID: 1; Lpar profile: vlpar1.prof;
HCP: HMC (hmc.cluster.net: 192.168.0.100)
Install Interface: eth0
OS: rhels5.2
Postscripts: setupntp (The scripts will be run after the installation)
Group: hmc,all (The node belong to these groups, then it will has the attributes of these groups as default)
Nodetype: compute (A common node. If you want to install a service node, the Nodetype should be “service”)

The attributes of Management node:
Hostname: pmanagenode
IP: 192.168.0.1
### Gather Node information using the rscan command
#### Define HMC as an xCAT node
First, we define the hardware control point of the nodes in the cluster database.
The following command will create an xCAT node definition for an HMC with a host name of “hmc01”. The groups, nodetype, mgt, username, and password attributes must be set.
mkdef –t node –o hmc01 groups=”all” nodetype=hmc mgt=hmc	username=hscroot password=abc123
#### Discover the LPARs managed by HMC
Use the rscan command to gather the LPAR information. This command can be used to display the LPAR information in several formats and can also write the LPAR information directly to the xCAT database. In this example we will use the “-z” option to create a stanza file that contains the information gathered by rscan as well as some default values that could be used for the node definitions.
To write the stanza format output of rscan to a file called “node.stanza” run the following command.
rscan –z hmc01 > node.stanza

This file can then be checked and modified as needed. For example you may need to add a different name for the node definition or add additional attributes and values.
Note: The stanza file will contain stanzas for things other than the LPARs. This information must also be defined in the xCAT database. It is not necessary to modify the non-LPAR stanzas in any way.
The stanza file will look something like the following.
Server-9117-MMA-SN10F6F3D:
        objtype=node
        nodetype=fsp
        id=5
        model=9118-575
        serial=02013EB
        hcp=hmc01
        pprofile=
        parent=Server-9458-10099201WM_A
        groups=fsp,all
        mgt=hmc

pnode1:
        objtype=node
        nodetype=lpar,osi
        id=9
        hcp=hmc01
        pprofile=lpar9
        parent=Server-9117-MMA-SN10F6F3D
        groups=all
        mgt=hmc

pnode2:
        objtype=node
        nodetype=lpar,osi
        id=7
        hcp=hmc01
        pprofile=lpar6
        parent=Server-9117-MMA-SN10F6F3D
        groups=all
        mgt=hmc

Note: The rscan command supports an option to automatically create node definitions in the xCAT database. To do this the LPAR name gathered by rscan is used as the node name and the command sets several default values. If you use the “-w” option make sure the LPAR name you defined will be the name you want used as your node name.
For a node which was defined correctly before, you can use the “lsdef –z [nodename]> node.stanza” command to export the definition into the node.stanza, and use command “cat node.stanza | chdef -z” to update the node.stanza according to your need.
#### Define xCAT node using the stanza file
The information gathered by the rscan command can be used to create xCAT node definitions.
Since we have put all the node information in a stanza file we can now pass the contents of the file to the mkdef command to add the definitions to the database.

cat node.stanza | mkdef –z

### Update the node definitions using the chtab command:
#### Modify the table nodelist
chtab node=”pnode1” nodelist.groups=hmc,all
#### Modify the table nodehm
This lpar of power5 use the HMC as the HCP

chtab node="pnode1" nodehm.power=hmc nodehm.mgt=hmc nodehm.cons=hmc
#### Modify the table noderes

chtab node="pnode1" noderes.netboot=yaboot noderes.tftpserver=192.168.0.1 noderes.nfsserver=192.168.0.1 noderes.monserver=192.168.0.1 noderes.installnic="eth0" noderes.primarynic="eth0" noderes.xcatmaster=192.168.0.1

Note: Please make sure the attributes "installnic" and "primarynic" are set up the correct Ethernet Interface of compute node. Otherwise the compute node installation may hang requesting information from an incorrect interface.
#### Modify the table nodetype
chtab node="pnode1" nodetype.os="rhels5.2" nodetype.arch="ppc64" nodetype.profile="compute" nodetype.nodetype="lpar,osi"

Note: This means when node: pnode1 is installed, it will install the rhels5.2 OS and architecture: ppc64.
#### Modify the table ppc and vpd
How to obtain the node attributes from the HMC
To achieve the ARCH attributes in example, we list all the lpar attributes of the node. You can follow these steps to obtain the lpar attributes of a new Lpar.

1. Login the HMC
2. Use the “ssh HMC-l hscroot id to login” .
3. Display the machines managed by this HMC
  lssyscfg -r sys
4. Display the lpars of the machine
  lssyscfg -r lpar -m Server-9117-MMA-SNxxxx
Modify the table ppc
chtab node="pnode1" ppc.hcp=hmc.cluster.net ppc.id=1 ppc.pprofile=vlpar1.prof ppc.parent=Server-9117-MMA-SNxxxx

Modify the table vpd
chtab node=Server-9117-MMA-SNxxxx vpd.serial=xxxx vpd.mtm=9117-MMA
Note: the mtm and serial num come from the output of 5.1.5.1
#### Modify the table chain
chtab node="pnode1" chain.node="pnode1" chain.currstate=boot chain.currchain=boot
#### Modify the table postscripts
chtab node=pnode1 postscripts.postscripts=setupntp
This only needs to be done, if you want NTP setup on the compute node.
## Setup the Management Node Services
### Update the networks table
EXAMPLE:
An interface which needs to be added:
eth1 Link encap:Ethernet HWaddr FE:99:72:0C:8B:04
        inet addr:192.168.0.1 Bcast:192.168.0.255 Mask:255.255.255.0
        inet6 addr: fe80::fc99:72ff:fe0c:8b04/64 Scope:Link
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:5373584 errors:0 dropped:0 overruns:0 frame:0
        TX packets:10583411 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:406081967 (387.2 MiB) TX bytes:15279683348 (14.2 GiB)
        Interrupt:20
You can use the chtab or tabedit command to add the network entry:
chtab net=192.168.0.0 networks.netname=net1 networks.mask=255.255.255.0 networks.mgtifname=eth1 networks.gateway=192.168.0.1 networks.dhcpserver=192.168.0.1 networks.tftpserver=192.168.0.1 networks.nameservers=192.168.0.1
### Setup the DNS
#### Setup /etc/hosts with entries for all you nodes, hmcs, fsps

127.0.0.1	localhost
192.168.0.1	pmanagenode
192.168.0.10	pnode1
#### Setup the nameserver
Add following lines into /etc/resolv.conf
search cluster.net
nameserver 192.168.0.1
#### Setup the DNS attributes in the Site table
chtab key=nameservers site.value=192.168.0.1 (Setup local machine as nameserver)
chtab key=forwarders site.value=9.114.1.1 (Setup the external nameserver)
chtab key=domain site.value=cluster.net (Setup the local domain)
#### Setup DNS configuration

makedns
service named start
chkconfig --level 345 named on
### Configure conserver
makeconservercf
service conserver restart
### Check rcons

rcons pnode1

If the output is:

Can't locate object method "stty" via package "IO::Tty" at /opt/xcat/lib/perl/xCAT/PPCcli.pm line xxx.
Download the package “perl-IO-Stty-.02-1.2.el5.rf.noarch.rpm” and install the package manually, following the step:

rpm -ivh perl-IO-Stty-.02-1.2.el5.rf.noarch.rpm
### Update the mac table with the address of the node(s)

If there's only one ethernet adapter on the node:
getmacs pnode1
But, if there're more than one ethernet adapters on the node, you have to specify more parameters like this:
getmacs pnode1 -S 192.168.0.1 -G 192.168.0.1 -C 192.168.0.10
The output looks like following:
pnode1:
 Type Location Code MAC Address Full Path Name Ping Result Device Type

ent U9133.55A.10E093F-V4-C5-T1 f2:60:f0:00:40:05 /vdevice/l-lan@30000005 virtual
### Check rpower is working to the node

rpower pnode1 stat
rpower pnode1 on/off
### Setup dhcp
#### Setup the site table dhcp interfaces
chtab key=dhcpinterfaces site.value='pmanagenode|eth1'
#### SLES: Install dhcp-server rpm
On the SLES management node, the dhcp-server rpm may not have been automatically installed. Verify that it is installed:
rpm -qa | grep -i dhcp-server

If it is not installed, installed it manually.
For RHEL:
yum install dhcp-server

For SLES:
zypper install dhcp-server

Also, verify that the sysconfig dhcpd configuration file has the DHCPD_INTERFACE value set correctly:
vi /etc/sysconfig/dhcpd
DHCPD_INTERFACE=”eth0”
replacing “eth0” with the correct interface for your management node.
#### Configure the DHCP
Add the relevant networks into the DHCP configuration:
makedhcp -n
Add the defined node into the DHCP configuration:

makedhcp -a
service dhcpd restart
Note: Please make sure there is only one dhcpd server running in the subnet

# Install a Compute Node
EXAMPLE:
Hostname: pnode1
IP: 192.168.0.10
Arch: ppc64 (An Lpar of power5); machine name: Server-9117-MMA-SNxxxx; Lpar ID: 1; Lpar profile: vlpar1.prof;
HCP: HMC (hmc.cluster.net: 192.168.0.100)
Install Interface: eth0
OS: rhels5.2
Postscripts: setupntp (The scripts will be run after the installation)
Group: hmc,all (The node belong to these groups, then it will has the attributes of these groups as default)
Nodetype: compute (A common node. If you want to install a service node, the Nodetype should be “service”)
The attributes of Management node:
Hostname: pmanagenode
IP: 192.168.0.1

An example for pnode1.stanza
lsdef -l pnode1
Object Name: pnode1
    arch=ppc64
    cons=hmc
    groups=hmc,all
    hcp=hmc.cluster.net
    id=1
    installnic=eth0
    mgt=hmc
    netboot=yaboot
    nodetype=lpar,osi
    os=rhels5.2
    parent=Server-9117-MMA-SNxxxx
    postscripts=setupntp
    power=hmc
    pprofile= vlpar1.prof
    profile=compute.ppc64
    primarynic=eth0
    xcatmaster=192.168.0.1
    tftpserver=192.168.0.1
    monserver=192.168.0.1
    nfsserver=192.168.0.1

Ensure that your nodes have similar attributes defined.
### Prepare the installation source
copycds /iso/RHEL5.2-Server-20080430.0-ppc-DVD.iso

Note: If you encounter the issue that the iso cannot be mounted by the copycds command. Make sure the SElinux is disabled. See .
### Diskfull/Statefull Node installation
#### Verify or create install template files
xCAT uses KickStart and AutoYaST install templates and other install files based on the “profile” attribute assigned to your compute node, and optionally the OS version and/or architecture. Sample profiles are shipped in the following directories:
For RedHate:
cd /opt/xcat/share/xcat/install/rh/

For SLES:
cd /opt/xcat/share/xcat/install/sles/

Our example uses the profile “compute” and will use the compute.tmpl and other compute.* files from this directory. If you would like to modify any of these sample files to customize the image for your nodes, copy all relevant files to
/install/custom/install/rh
or
/install/custom/install/sles

If you would like to create different images for different types of compute nodes, create separate sets of files in this directory naming the files <profile>.* to match the image name you wish to use.

Check to make sure the <profile>.tmpl contains the correct OS installer information that you need for your nodes. You can change the OS packages, install harddrives and other devices, and any other information you choose.

You can also place other application and user rpms into the following directory:
/install/post/otherpkgs/<os>/<arch>

Then list the packages to be installed from that directory onto the node as part of xCAT postscripts processing by specifiying them in the file
/install/custom/install/sles/<profile>.otherpkgs.pkglist
See the xCAT Updatenode documentation for more details.
#### SLES 11: Copy stunnel rpm from xcat deps
XCAT requires the stunnel rpm to be installed on the node to properly process postscripts. The stunnel rpm is no longer shipped with SLES 11 (it is shipped with earlier versions of SLES). Therefore, you need to put a copy of this package into the following directory:
mkdir -p /install/post/otherpkgs/sles11/ppc64
You can either download and build the source yourself getting the latest version from: http://www.stunnel.org/download/source.html.
Or you can download a prebuilt copy available with the xCAT OSS dependencies:
cd /install/post/otherpkgs/sles11/ppc64
wget http://xcat.sourceforge.net/yum/xcat-dep/sles11/ppc64/stunnel*.rpm

Make sure you have a <profile>.otherpkgs.pkglist file which has at least the following package to install
    stunnel

#### Set the node status
nodeset "pnode1" install
#### Reboot to start the installation
rpower "pnode1" boot
#### Check the installation results
1. SSH service on the node is working and you can login without a password
2. If ssh is not working, force exchange the ssh key to the compute node using xdsh:
xdsh pnode1 -K

Note: If you cannot ssh into the node without a password, then when you run this command to exchange the keys. At that point you should be able to run

xdsh pnode1 date
### Install a Diskless/Stateless Compute node

#### Generate the stateless image for compute node
Typically, you can build your stateless compute node image on the Management Node if it will have the same OS and architecture. If you need another OS image or architecture than is installed on the Management Node, you will need a machine that meets the architecture you want for the image and create the image on that node.
#### Check the compute node packaging list
xCAT uses package lists and other templates based on the “profile” attribute assigned to your compute node, and optionally the OS version and/or architecture. Sample profiles are shipped in the following directories:
For RedHate:
cd /opt/xcat/share/xcat/netboot/rh/

For SLES:
cd /opt/xcat/share/xcat/netboot/sles/

Our example uses the profile “compute” and will use the compute.pkglist, compute.exlist, and other compute.* files from this directory. If you would like to modify any of these sample files to customize the image for your nodes, copy all relevant files to
/install/custom/netboot/rh
or
/install/custom/netboot/sles

If you would like to create different images for different types of compute nodes, create separate sets of files in this directory naming the files <profile>.* to match the image name you wish to use.

Check to make sure the <profile>.exlist excludes the packages you want to exclude.

Check to make sure <profile>.pkglist has at least the following packages to install
    bash
    nfs-utils
    stunnel
    dhclient
    kernel
    openssh-server
    openssh-clients
    busybox-anaconda
    wget
    vim-minimal
    ntp

And add any other packages you would like to install on your compute node. For example, if you want to have userids with passwords you should add the following:
    cracklib
    libuser
    passwd

For SLES11, the pkglist files are different. Make sure to start with a copy of commpute.sles11.ppc64.pkglist and compute.sles11.ppc64.otherpkgs.pkglist for your SLES11 images. And make sure your <profile>.pkglist has at a minimum the following packages to install
    aaa_base
    bash
    nfs-utils
    dhcpcd
    kernel-ppc64
    openssh
    psmisc
    wget
    sysconfig
    syslog-ng
    klogd
    vim

Make sure you have a <profile>.otherpkgs.pkglist file which has at least the following package to install
    stunnel

Since the stunnel rpm does not ship with base SLES11, you need to put a copy of this package into the following directory:
 mkdir -p /install/post/otherpkgs/sles11/ppc64
You can either download and build the source yourself getting the latest version from: http://www.stunnel.org/download/source.html.
Or you can download a prebuilt copy available with the xCAT OSS dependencies:
cd /install/post/otherpkgs/sles11/ppc64
wget http://xcat.sourceforge.net/yum/xcat-dep/sles11/ppc64/stunnel*.rpm

You can also place other application and user rpms into the otherpkgs directory and list the packages to be installed into the image in the <profile>.otherpkgs.pkglist file. See the xCAT Updatenode documentation for more details.

You may also have a <profile>.postinstall file. This is a script that will be run against the generated image after all rpms have been installed. You can put whatever customization code you require that should be run every time this image is generated.
#### Run image generation
cd /opt/xcat/share/xcat/netboot/rh
./genimage -i eth0 -n ibmveth -o rhels5.2 -p compute

For SLES11:
./genimage -i eth0 -n ibmveth -o sles11 -p compute

#### Pack the image
packimage -o rhels5.2 -p compute -a ppc64
or for SLES
packimage -o sles11 -p compute -a ppc64
#### Set the node status
nodeset "pnode1" netboot
#### Reboot to start the installation
rpower "pnode1" boot
#### Check the installation result
SSH service to the compute node is working. You can ssh login without a password.
# Perform Firmware upgrades for CEC on P5/P6

Requirements:
POWER5 and POWER6 Licensed Internal Code updates must meet the following prerequisites:
  1. Enable the HMC to allow remote ssh connections.
  2. Ensure that ssh is installed on the AIX xCAT management node. If you are using an AIX management node, make sure the value of "useSSHonAIX" is “yes” in the site table.
    chtab key="useSSHonAIX" site.value=yes
  3. The Lpar , CEC, or BPA has been defined in the nodelist, nodehm,nodetype,vpd, ppc tables
  4. Define the HMC related the above node as a node on the management node. For example,
    nodeadd hmc01.clusters.com groups=hmc
  5. Setup SSH connection to HMC
  Run the rspconfig command to set up and generate the ssh keys on the xCAT management node and transfer the public key to the HMC. You must also manually configure the HMC to allow remote ssh connections. For example:
  rspconfig hmc01.clusters.com sshcfg=enable
  6. Get the Microcode update package and associated XML file.
## Define the CEC as a node on the management node .
Update the xCAT required xCAT tables:
Modify the nodelist table
nodeadd Server-m_tmp-SNs_tmp groups=hmc,all

Modify the table nodehm
chtab node="Server-m_tmp-SNs_tmp" nodehm.mgt="hmc"

Modify the table nodetype:
chtab node="Server-m_tmp-SNs_tmp" nodetype.nodetype="fsp"

Modify the table ppc:
chtab node="Server-m_tmp-SNs_tmp" ppc.hcp= hmc01.clusters.com

Modify the tab vpd:
chtab node=Server-m_tmp-SNs_tmp vpd.serial=s_tmp vpd.mtm=m_tmp

Set the account of the HMC(Modify the ppchcp):
chtab hcp=hmc01.clusters.com ppchcp.username=hscroot ppchcp.password=abc123
## Setup SSH connection to HMC
      Generate the ssh keys on the xCAT management node and transfer the public key to the HMC to configure the HMC to allow remote ssh connections.

rspconfig hmc01.clusters.com sshcfg=enable
## Check firmware level
rinv Server-m_tmp-SNs_tmp firm

### Update the firmware

 Download the Microcode update package and associated XML file from the IBM Web site: http://www14.software.ibm.com/webapp/set2/firmware/gjsn. Create the /tmp/fw directory, if necessary, and copy the downloaded files to the /tmp/fw directory.
   Run the rflash command with the --activate flag to specify the update mode to perform the updates.（Please see the “rflash” manpage for more information）
rflash Server-m_tmp-SNs_tmp -p /tmp/fw --activate disruptive

NOTE:You Need check your update is concurrent or disruptive here!! other commands sample:
rflash Server-m_tmp-SNs_tmp -p /tmp/fw --activate concurrent

Notes:
1. If the noderange is the group lpar, the upgrade steps are the same as the CEC's.
2. System p5 and p6 updates can require time to complete and there is no visual indication that the command is proceeding.

# Perform Firmware upgrades for BPA on P5/P6

## Define the BPA as a node on the management node.

Update the xCAT tables:

Modify the nodelist table. Define the BPA as a node
nodeadd Server-m_tmps_tmp groups=hmc,all

Modify the table nodehm
chtab node="Server-m_tmps_tmp" nodehm.mgt="hmc"

Modify the table nodetype:
chtab node="Server-m_tmps_tmp" nodetype.nodetype="fsp"

Modify the table ppc:
chtab node="Server-m_tmps_tmp" ppc.hcp= hmc01.clusters.com ppc.id=x

Modify the tab vpd:
chtab node=Server-m_tmps_tmp vpd.serial=s_tmp vpd.mtm=m_tmp

Set the account of the HMC(Modify the ppchcp):
chtab hcp=hmc01.clusters.com ppchcp.username=hscroot ppchcp.password=abc123

## Setup SSH connection to HMC
Generate the ssh keys on the xCAT management node and transfer the public key to the HMC to configure the HMC to allow remote ssh connections.
rspconfig hmc01.clusters.com sshcfg=enable
## User rinv to check the firmware level ( see rinv manpage).
        rinv Server-m_tmps_tmp firm

## Update the firmware

Download he Microcode update package and associated XML file from the IBM Web site:
        http://www14.software.ibm.com/webapp/set2/firmware/gjsn.
Create the /tmp/fw directory, if necessary, and copy the downloaded files to the /tmp/fw directory.
Run the rflash command with the --activate flag to specify the update mode to perform the updates.

rflash Server-m_tmps_tmp -p /tmp/fw --activate disruptive

NOTE:You Need check your update is concurrent or disruptive here!! other commands sample:
rflash Server-m_tmps_tmp -p /tmp/fw --activate concurrent

### Commit currently activated LIC update(copy T to P) for a CEC of HMC-attached System p5 and p6
1. See steps ( 1 – 5) under Perform Firmware upgrades for BPA on P5/P6 requirements..
2. Check the output of the last step, to check whether the LIC will be committed. If yes the run the rflash command with the –commit flag.
rflash Server-m_tmp-SNs_tmp --commit

Notes:
1. If the noderange is BPA/Lpar, the commit steps are the same as the CEC's.
2. When the –commit or --recover two flags is used, the noderange cannot be BPA . It only can be CEC or LPAR ,and will take effect for both managed systems and power subsystems.